## Slide 1: Enhanced Interior Gateway Routing Protocol (EIGRP)
Mumtaz Ahmad

## Slide 2: Table of Contents
EIGRP Overview
EIGRP DUAL Algorithm
EIGRP Messages
EIGRP Tables
Classless Protocol
VLSM Support
EIGRP Metrics
EIGRP Administrative Distance
RTP for Reliable Delivery

## Slide 3: EIGRP Overview
EIGRP Protocol is one of the most used Dynamic Routing Protocol as IGP (Interior Gateway Protocol). Especially it is used for Routing purpose inside the networks that is mostly consist of Cisco devices.
EIGRP (Enhanced Interior Gateway Routing Protocol) is a Hybrid Routing Protocol that contains the best features of both Distance Vector and Link-State Routing Protocol properties. It was developed by Cisco as an enhancement to IGRP (Interior Gateway Routing Protocol) and as a Cisco proprietary protocol and it is only available on Cisco devices.

## Slide 4: EIGRP DUAL Algorithm
EIGRP uses DUAL (Diffusing Update Algorithm) for routing calculations. Periodic Updates are not used but if a change occurs in the network like up/down links, update messages are sent.
With DUAL Algorithm, Topology table is built. In Topology Table both the Best Routes and the Backup Routes to a destination are stored. This provides a Fast Convergence Mechanism.

## Slide 5: EIGRP DUAL Algorithm
Enhanced Interior Gateway Routing Protocol keeps the “Backup Routes”.
The 2nd “Best Route” to a destination kept in Topology table. So, during a failure of a link or route, it does not need to calculate a new route. It uses the Backup Route towards the destination.

## Slide 6: EIGRP Messages
EIGRP uses different types of messages to build neighborship, to keep the connection and for the updates. These main messages are :
Hello
Update
Query
Reply
Ack

## Slide 7: EIGRP Messages
Hello Packets are used to establish and maintain EIGRP Neighborship.
Update Packets are used to send routing updates.
Query Packets are used to ask for any routing update, requests an update.
Reply Packets are used as a response to the Query Packets.
ACK Packets are used as a feedback to the Update, Query or Reply packets as a feedback mechanism.

## Slide 8: EIGRP Tables
Enhanced Interior Gateway Routing Protocol has three tables. These tables are used on Routing Operations. These tables are given below:
Neighbor Table
Topology Table
Routing Table

## Slide 9: EIGRP Tables
Neighbor Table is the table that keeps All EIGRP Neighbor Routers.
Topology Table is the table that keeps All Routes to all the destinations
Routing Table is the table that keeps the Best Routes to any destinations.

## Slide 10: Classless Protocol
EIGRP is a Classless Routing Protocol.
It sends the subnet masks in the Update Packets.

## Slide 11: VLSM Support
EIGRP also supports VLSM (Variable Length Subnet Mask).
Different Subnet Masks can be used with this protocol.
By using VLSM, it is a protocol that uses the IP addresses range efficiently.

## Slide 12: EIGRP Metrics
EIGRP uses a very complex metric by using
Bandwidth
Load
Delay
Reliability
MTU

## Slide 13: EIGRP Metrics
There are some K values in EGRP metric formula. By default these values are:
K1 (Bandwidth) = 1 K2 (Load) = 0 K3 (Delay) = 1 K4(Reliability) = 0 K5(MTU) = 0
*** These K values need to be match in both ends to form an EIGRP Neighborship.
*** You can change these values but it is not recommended.

## Slide 14: EIGRP Metrics
By default Bandwidth and Delay are used as a metric the other values will be 0, because of multiplying with 0). So, EIGRP uses the path with minimum bandwidth and the total delay to a destination.

## Slide 15: EIGRP Metrics
By default Bandwidth and Delay are used as a metric the other values will be 0, because of multiplying with 0). So, EIGRP uses the path with minimum bandwidth and the total delay to a destination.

## Slide 16: EIGRP Administrative Distance
The Administrative Distance values for EIGRP are given below:
Internal : 90
External : 170
Summary : 5
*** If there are routes to a destination with Enhanced Interior Gateway Routing Protocol, RIP and OSPF, EIGRP (Internal) Routes are preferred over RIP and OSPF Routes. Because the administrative distance of RIP is 120 and OSPF Administrative Distance is 110.

## Slide 17: RTP for Reliable Delivery
EIGRP uses RTP (Reliable Transport Protocol) to control sending and acknowledging messages.
RTP ensures delivery of packets.
RTP is used by Update, Query and Reply packets.
Hello and Ack packets do not use RTP.