## Slide 1: CSC- 362 Computer Networks Week:12 Lecture:19 - 22
                Prepared by:
                Mr. Attique Ur Rehman

## Slide 2: Internetworking

## Slide 3: The Big Picture
You are here

## Slide 4
Internetworking
Outline
  Fragmentation, Reassembly, Forwarding and Routing

## Slide 5: Fragmentation and Reassembly
Different physical layers provide different limits on frame length (maximum transfer unit - MTU)
Source host cannot know minimum value along dynamic route (no signaling)
Avoid restricting datagram size to a small value
Solution: when necessary, split IP packet into fragments before sending over physical link
Questions
  Where should reassembly occur ?
  What happens when a fragment is damaged/lost ?

## Slide 6: Fragmentation and Reassembly
Strategy used with IP
  Fragments are self-contained IP datagrams
  Avoid fragmentation at source host
    Transport layer passes small enough packets to fit into MTU of local network
    MTU on ATM based on CS-PDU (not cells)
  Re-fragmentation along the path is possible
  Reassemble at destination to minimize re-fragmentation
  Drop packet if one or more fragments lost (based on timeout); do not recover from lost fragments
PDU: Protocol Data Unit
SDU: Service Data Unit
CS-PDU: Convergence Sub-layer Protocol Data Unit
Maximum large frame size
FDDI: 4,352 bytes
Ethernet: 1500 bytes

## Slide 7: Fragmentation and Reassembly Example
Ident
= x
Offset
= 0
Start of header
0
Rest of header
1400 data bytes
Ident
= x
Offset
= 0
Start of header
1
Rest of header
512 data bytes
Ident
= x
Offset
= 64
Start of header
1
Rest of header
512 data bytes
Ident
= x
Offset
= 128
Start of header
0
Rest of header
376 data bytes
Assume MTU for Ethernet= 1500 bytes FDDI= 4500 bytes PPP = 532 bytes
1420 byte datagram = 1400 byte data + 20 byte IP header
Offset = 512/8 = 64
Offset = 2*512/8 = 128

## Slide 8: Datagram Forwarding
Hosts and routers maintain forwarding tables
Forwarding table maps network number to next hop
  List of (network/host, next hop) pairs
Table often ends with default router
  Recall hierarchical routing notion of handing unknown addresses up to the next level
Very simple (and static) table on hosts
Complex (and dynamic) table on routers
Example (R2)
Network Number Next Hop
1 R3
2 R1
3 interface 1
4 interface 0

## Slide 9: Datagram Forwarding
Concatenation of networks
Protocol stack
Network 2
Ethernet
Network 3
FDDI
Network 1
Ethernet
R1
R2
R3
H8
H2
H3
H1
H4
H5
H6
H7
Network 4
Point
-to-
point
R1
H1
TCP
IP
ETH
ETH
PPP
IP
R2
PPP
FDDI
IP
R3
FDDI
ETH
IP
H8
TCP
IP
ETH
PPP: Point to Point Protocol FDDI: Fiber Distributed Data Interface
Network # | Next Hop
1 | R3
2 | R1
3 | Interface 1
4 | Interface 0
IP

## Slide 10: Datagram Forwarding
Network # Netmask Next hop / port
18.0.0.0 255.0.0.0 1
128.32.0.0 255.255.0.0 2
0.0.0.0 0.0.0.0 3
dest: 18.26.10.0
mask with 255.0.0.0
matched! send to port 1
dest: 128.16.14.0
mask with 255.0.0.0
not matched
mask with 255.255.0.0
not matched
mask with 0.0.0.0
matched! send to port 3

## Slide 11: Datagram Forwarding
Every datagram contains destination’s address
Network portion of address is compared with pairs in the forwarding table
If directly connected to destination network, then forward to host
If not directly connected to destination network, then forward to some (default) router
In both the cases (sending directly or indirectly to host), use Address Resolution Protocol (ARP) to pass to physical layer

## Slide 12: Routing
How do routers acquire information in their forwarding tables ?
  Algorithms
  Scalability

## Slide 13: Routing
A stranger appears and asks “Airport ”
Which way do you point ?
Lahore/ Shahdara
Airport
Babo sabo
Thokar
Wapda Town
Kalma Chowk

## Slide 14: What is Routing ?
Definition: task of constructing and maintaining forwarding information (in hosts or in switches)
Goals for routing
  Capture notion of “best” routes
  Propagate changes effectively
  Require limited information exchange
  Admit efficient implementation
Important notion: graph representation of network

## Slide 15: Forwarding vs Routing
Forwarding: to select an output port based on destination address and routing table
Routing: process by which routing table is built
Forwarding table: enough information to accomplish the forwarding function; optimized for forwarding
Routing table: built by routing algorithms to build forwarding table; optimized for topology changes
Routing Table:
  Network # (10) - Next hop (171.69.245.10)
Forwarding Table:
  Network # (10) - interface (if0) - MAC (8:0:2b:e4:b:1:2)

## Slide 16: Routing Overview
Hierarchical routing infrastructure defines routing domains
  Where all routers are under same administrative control
Network as a Graph
  Nodes are routers
  Edges are links
  Each link has a cost
Problem: Find lowest cost path between two nodes
  Maintain information about each link
  Static: topology changes are not incorporated
  Dynamic (or distributed): complex algorithms

## Slide 17: Ideal Approach to Routing
Maintain information about each link
  For each direction: bandwidth, latency and queuing delay
Calculate fastest path between each directed pair
  Function of packet size

## Slide 18: Problem with Ideal Routing
Unbounded amount of information
Queuing delay can change rapidly
Graph connectivity changes, too
Solution: Dynamic algorithm
  Periodically recalculate routes
  Distributed algorithm
    No single point-of-failure
    Reduced computation per node
  Abstract “distance” metric
    Combines many factors

## Slide 19: Routing Outline
Algorithms
  Static shortest path algorithms
    Bellman-Ford—all pairs shortest paths to destination
    Dijkstra’s algorithm—single source shortest path
  Distributed, dynamic routing algorithms
    Distance vector routing (based on Bellman-Ford)
    Link state routing (Dijkstra’s algorithm at each node)
Metrics (from ARPANET, with informative names)
  Original
  New
  Revised

## Slide 20: Bellman-Ford Algorithm
Static, centralized algorithm, (local iterations/dest)
Requires: directed graph with edge weights (costs)
Calculates: shortest paths for all directed pairs
Check use of each node as successor in all paths
For every node N
  for each directed pair (B,C)
    is the path B  N  …C better than B .C ?
    is cost BNdest smaller than previously known ?
For N nodes
  Uses an NxN matrix of (distance, successor) values

## Slide 21: Bellman-Ford Algorithm
After n iterations, nodes at distance n hops along the shortest path have correct information
6
2
2
5
1
1
1
source
destination
A
B
C
E
infinity
infinity
infinity
infinity
infinity
infinity
infinity
1 Dest
5 Dest
infinity
1 Dest
3 B
infinity
5 Dest
7 E
1 Dest
3 B
8 C
4 A
7 E
7 C
3 B
1 Dest
4 A
6 E

## Slide 22: Dijkstra’s Algorithm
Static, centralized algorithm, build tree from source
Requires directed graph with edge weights (distances)
Calculates: shortest paths from one node to all others
Greedily grow set S of known minimum paths
From node N
  Start with S = {N} and one-hop paths from N
  Loop n-1 times
    add closest outside node M to S
    for each node P not in S
      is the path N .....M .P better than N.... P ?

## Slide 23: Dijkstra’s Algorithm
1
1
1
2
2
2
2
2
3
3
3
3
4
4
6
6
7
7
8
10
9
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15

## Slide 24: Distance Vector Routing
Distributed, dynamic version of Bellman-Ford
Each node maintains distance vector: set of triples
  (Destination, Cost, NextHop)
  Edge weights starting at a node assumed known by that node
Exchange updates of distance vector (Destination, Cost) with directly connected neighbors (known as advertising the routes)
  periodically (on the order of several seconds to minutes)
  whenever vector changes (called triggered update)
The distance vector algorithm was the original ARPANET routing algorithm.
It was implemented more widely in local area networks with the Routing Information Protocol (RIP)

## Slide 25: Distance Vector Routing
Update local table if receive a “better” route
  Newly advertised route has smaller cost (shorter)
  Came from next-hop (successor advertising new one)
Refresh existing routes; delete if they time out
Local failure detection
  Control message not ACK’d
  Time out on periodic route update
Used in original ARPANET (until 1979)
Early Internet: Routing Information Protocol (RIP)
Early versions of DECnet and Novell IPX

## Slide 26: Distance Vector Routing Example
Information in routing table of each node:
  Iteration 1
At distance to reach node
node A B C D E F G
A 0 1 1 x 1 1 x
B 1 0 1 x x x x
C 1 1 0 1 x x x
D x x 1 0 x x 1
E 1 x x x 0 x x
F 1 x x x x 0 1
G x x x 1 x 1 0

## Slide 27: Distance Vector Routing Example
Information in routing table of each node:
  Iteration 2
At distance to reach node
node
A B C D E F G
A 0 1 1 2 1 1 2
B 1 0 1 2 2 2 x
C 1 1 0 1 2 2 2
D 2 2 1 0 x 2 1
E 1 2 2 x 0 2 x
F 1 2 2 2 2 0 1
G 2 x 2 1 x 1 0

## Slide 28: Distance Vector Routing Example
Information in routing table of each node:
  Iteration 3
At distance to reach node
node A B C D E F G
A 0 1 1 2 1 1 2
B 1 0 1 2 2 2 3
C 1 1 0 1 2 2 2
D 2 2 1 0 3 2 1
E 1 2 2 3 0 2 3
F 1 2 2 2 2 0 1
G 2 3 2 1 3 1 0

## Slide 29: Distance Vector Routing Table
Routing table at node B:
Destination Cost NextHop
A 1 A
C 1 C
D 2 C
E 2 A
F 2 A
G 3 A

## Slide 30: Distance Vector Routing: Link Failure
F detects that link to G has failed
F sets distance to G to infinity and sends update to A
A sets distance to G to infinity since it uses F to reach G
A receives periodic update from C with 2-hop path to G
A sets distance to G to 3 and sends update to F
F decides it can reach G in 4 hops via A

## Slide 31: Count to Infinity Problem
Link from A to E fails
A advertises distance of infinity to E, but B and C advertise a distance of 2 to E !
B decides it can reach E in 3 hops; advertises this to all
A decides it can read E in 4 hops; advertises this to all
C decides that it can reach E in 5 hops…
We are counting to infinity …

## Slide 32: Count to Infinity Problem
Node X notices that its link to Y is broken
Other nodes believe that the route through X is still good
Mutual deception !!!
How to solve this problem ?

## Slide 33: Network Diameter
The longest of all the calculated shortest paths in a network. It is the shortest distance between the two most distant nodes in the network.
The shortest path length from every node to all other nodes is calculated, the diameter is the longest of all the calculated path lengths

## Slide 34: Diameter of the Internet
Connect all nodes of a network in a big ring
  Network diameter will be half the ring circumference
Adding more links bring down network diameter
  Diameter can be quarter of the ring with one link …
How many links should be added to bring the diameter below some threshold ?

## Slide 35: Heuristic Attempts at Solution
Limit infinity to network diameter +1
  Small limit allows fast completion of counting to infinity
  Limits network size and growth!!!
Do not advertise routes to successors (Split Horizon)
  If route to A goes to B, do not inform B about route to A
  Solve mutual deception problem
Split horizon with poison reverse
  Advertise negative routes to node, learned from that node
  Poisoned the routes sent by the neighbors
Wait before advertising delays convergence

## Slide 36: Split Horizon
Avoid counting to infinity by solving “mutual deception” problem
When sending an update to node X, do not include destinations that you would route through X
  If X thinks route is not through you, no effect
  If X thinks route is through you, X will timeout route
A
B
C
D
C : 1 : C
C : 2 : B
C : ∞ : -
C : 2 : B
Loop of > 2 nodes fails split horizon !!!

## Slide 37: Split Horizon with Poison Reverse
When sending update to node X, include destinations that you would route through X with distance set to infinity
Don’t need to wait for X to timeout
RIP uses split horizon with poison reverse technique to reduce the chance of forming loops

## Slide 38: Distance Vector Routing Problems
Problems with DVR
  Information propagates slowly
  One period per hop for new routes
  Count to infinity for lost routes (mutual deception)
Loop free DVR protocols
  EIGRP
  DSDV
  Babel

## Slide 39: Link State Routing
Distributed, dynamic form of Dijkstra’s algorithm
Strategy
  Send to all nodes (not just neighbors) information about directly connected nodes (not entire route table) in LSP
Basic data structure: Link State Packet (LSP)
  ID of the node that created the LSP
  Cost of link to each directly connected neighbor: vector of (distance, successor) values
  Sequence number (SEQNO)
  Time-to-live (TTL) for this packet

## Slide 40: Link State Routing
Each node maintains a list of (ideally all) LSP’s
  Runs Dijkstra’s algorithm on list
  May discover its neighbors by “Hello” messages
Information acquisition via reliable flooding
  Create new LSP periodically; send to 1-hop neighbors
    Increment SEQNO (start SEQNO at 0 when reboot)
  Store most recent (higher SEQNO) LSP from each node
  Forward new LSP to all nodes but the one that sent it
    Decrement TTL of each LSP; discard when TTL=0
  Try to minimize routing traffic “overhead”

## Slide 41: Reliable Flooding
X
A
C
B
D
(a)
X
A
C
B
D
(b)
X
A
C
B
D
(c)
X
A
C
B
D
(d)

## Slide 42: Link State Routing
TTL fixes sequence number problems
  Wraparound, bit errors, host crashes
Used in
  ARPANET: bad heuristics brought down network in 1981
  Internet: Open Shortest Path First (OSPF)
  Intermediate System-Intermediate System (IS-IS)
    Designed for DECnet
    Adopted by ISO for connectionless network layer protocol (CNLP)
    Used in NSFNET backbone (and others) some digital cellular systems
    Minor variant in Novell NetWare

## Slide 43: Route Calculation: Dijkstra’s Shortest Path Algorithm
Let
  N denotes set of nodes in the graph
  l (i, j) denotes non-negative cost (weight) for edge (i, j)
  s denotes this node
  M denotes the set of nodes incorporated so far
  C(n) denotes cost of the path from s to node n
M = {s}
for each n in N - {s}
  C(n) = l(s, n) // calculate cost to each node
while (M != N)
  M = M union {w} such that C(w) is the minimum for
  all w in (N - M)
  for each n in (N - M)
    C(n) = MIN(C(n), C (w) + l(w, n ))

## Slide 44: Link State Routing
At each router, perform a forward search algorithm
Router maintains two lists
  Tentative
  Confirmed
Each list contains triplets
  <destination, cost, nexthop>

## Slide 45: Link State Algorithm
Initialize confirmed with entry for self (cost = 0)
For node just added in the confirmed list, select its LSP
For each neighbor of next, calculate cost to reach neighbor as the sum of cost from self to next and from next to neighbor
  If neighbor is currently in neither confirmed nor tentative, add <neighbor, cost, nexthop> to tentative, where nexthop is the direction to reach next
  If neighbor is currently in tentative and cost is less than current cost for neighbor , then replace current entry with <neighbor, cost, nexthop>, where nexthop is the direction to reach next
If tentative is empty, stop. Otherwise pick entry from tentative with the lowest cost, move it to confirmed and return to step 2.

## Slide 46: Route Calculation
At node D
Confirmed list Tentative list
(D,0,-)
(D,0,-) (C,2,C), (B,11,B)
(D,0,-), (C,2,C) (B,11,B)
(D,0,-), (C,2,C) (B,5,C), (A,12,C)
(D,0,-), (C,2,C), (B,5,C) (A,12,C)
(D,0,-), (C,2,C), (B,5,C) (A,10,C)
(D,0,-), (C,2,C), (B,5,C), (A,10,C)
D
A
B
C
5
3
2
11
10

## Slide 47: OSPF Routing Protocol
Authentication of routing messages
  Encrypted communication between routers
Additional hierarchy
  Domains are split into areas
  Routers only need to know how to reach every node in a domain
  Routers need to know how to get to the right area
  Load balancing
    Allows traffic to be distributed over multiple routes

## Slide 48: Link State Routing - Scalability
Stabilizes quickly, does not generates much traffic, responds to changes or node failures
One LSP per router in Internet (one vector element for every link): stored information is large!
Solution: hierarchical routing
  Split hosts into domains
  Routing occurs in two ways
    Within domains (scales as size of domain)
    Between domains (scales as number of domains)
  Add more levels as necessary
  Organize names (IP addresses) by routing domains

## Slide 49: Hierarchical Routing Drawbacks
Slightly inaccurate information
Cannot distribute heavy loads
hierarcical path
shortest path

## Slide 50: Comparison of Routing Approaches
Distance Vector
  Communicate information to neighbors only
  Exchange information about entire network
  RIP v1 and v2
    Scalability
Link State
  Communicate information to entire network
  Exchange information about neighbors only
  OSPF
    Mostly used

## Slide 51: Link State Metrics
Capture a general notion of distance
A heuristic combination of (among other factors)
  Distance, Bandwidth
  Average traffic
  Queue length
  Measured delay
A few to discuss
  Original ARPANET
  New ARPANET
  Revised ARPANET

## Slide 52: Example
Problem: Consider a network in which Router 3 has just come up after a long time. Please create a routing table for node 3.
Dijkstra's Algorithm
Bellman Ford Algorithm

## Slide 53: Dijkstra's Algorithm

## Slide 54: Bellman Ford Algorithm