## Slide 1: CSC- 362 Computer Networks Week:13 Lecture: 25 - 26
                Prepared by:
                Mr. Attique Ur Rehman

## Slide 2: Subnetting and Supernetting

## Slide 3: Virtual Geographies
Internet domain names (understood by people)
IP network numbers (understood by routers)
Internet domain name hierarchy
  ASCII strings separated by periods; typical formats are:
    host.domain.domain_type
      xyz.carepvtltd.com
    host.subdomain.domain.domain_type
      abc.cs.berkeley.edu
    host.domain.domain_type.country
      www.case.edu.pk

## Slide 4: Virtual Geographies and IP Address
Routers use IP network numbers
Original intention:
  One network number per physical network
Closer to real geography (than domain names)
Some jumps, e.g.,
  Divisions of one company
  Organizations with network research testbeds
Class
Network
Host
IP address

## Slide 5: Virtual Geographies and DNS
Translation from domain name to IP address
  Domain to IP: domain name service (DNS)
  IP to domain: relies on host
    Not secure
    Use reverse lookup - domain to IP - for security
DNS is a hierarchical, (mostly) distributed application (more detail later)

## Slide 6: Scaling Problems for the Internet
Inefficient address allocation (by class system)
Too many networks for routing
Can trade off between these two
Questions
  What network(s) should you allocate to a company with 1000 machines ?
  What about a company with 200 machines ?
  What about a company with 2 machines that plans to grow rapidly ?

## Slide 7: Scaling Problems for the Internet
Pressure primarily on class B networks
  Most companies plan to grow beyond 255 machines
  Renumbering is a hassle and can interrupt service
  Only around 16,000 class B networks available (14 bits)
Class B networks aren’t very efficient
  Few organizations have O(10,000) machines
  More likely a network uses O(1,000) of 65,000 addresses
Scaling problems with alternatives
  Multiple table entries if class C networks used instead
  Protocols do not scale beyond O(10,000) networks

## Slide 8: IP Address Hierarchy Evolution
Begin with class-based system
Subnetting within an organization
  Network can be broken into smaller networks
  Recognized only within the organization
  Implemented by packet-switching
  Smaller networks called subnets
class A:
0
network (7)
host (24 bits)
class B:
1
network (14 bits)
host (16 bits)
0
class C:
1
network (21 bits)
host (8 bits)
1
0

## Slide 9: Subnetting
Subnetting is the strategy used to partition a single physical network into more than one smaller logical sub-networks (subnets)
A subnet is a logical partition of an IP network into multiple, smaller network segments.
Another level to address/routing hierarchy: subnet
Subnet masks define variable partition of host part
Subnets visible only within site (close to each other)

## Slide 10: Subnetting
Class
Network
Host
IP address
Network
Host
Subnetted IP address
Subnet
1111111111111111
00000000
Subnet mask
11111111
Class
11
1111111111111111
0000
Non-contiguous mask
1111
11
1111
0000

## Slide 11: Example
Problem: Your company has bought IP 201.0.0.0 from IANA. Design a network for your company that has 20 departments. All of them should be on separate subnets
• What will be the subnet mask?
• What is the first IP address of the first, second and last subnet
• What is the last IP address of the first, second and last subnet
• Also write the broadcast address of all the subnets

## Slide 12: Example
Solution:
IP=201. 0 . 0 . 0
1100 1001 . 0000 0000 . 0000 0000 . 0000 0000
201 => Class C IP Address = > 24 Network Bits and 8 Host Bits
=> No_of_bits_for_sub-netting = 5
Subnet Mask
1111 1111 . 1111 1111 . 1111 1111 . 1111 1000
255.255.255.248

## Slide 13: Example
First Subnet:
Subnet Address:
1100 1001 . 0000 0000 . 0000 0000 . 0000 1000
201.0.0.8
First IP:
1100 1001 . 0000 0000 . 0000 0000 . 0000 1001
201.0.0.9
Last IP:
1100 1001 . 0000 0000 . 0000 0000 . 0000 1110
201.0.0.14
Broadcast Address:
1100 1001 . 0000 0000 . 0000 0000 . 0000 1111
201.0.0.15

## Slide 14: Example
Second Subnet:
Subnet Address:
1100 1001 . 0000 0000 . 0000 0000 . 0001 0000
201.0.0.16
First IP:
1100 1001 . 0000 0000 . 0000 0000 . 0001 0001
201.0.0.17
Last IP:
1100 1001 . 0000 0000 . 0000 0000 . 0001 0110
201.0.0.22
Broadcast Address:
1100 1001 . 0000 0000 . 0000 0000 . 0001 0111
201.0.0.23

## Slide 15: Example
Last Subnet:
Subnet Address:
1100 1001 . 0000 0000 . 0000 0000 . 1111 0000
201.0.0.240
First IP:
1100 1001 . 0000 0000 . 0000 0000 . 1111 0001
201.0.0.241
Last IP:
1100 1001 . 0000 0000 . 0000 0000 . 1111 0110
201.0.0.46
Broadcast Address:
1100 0011 . 1010 1000 . 0000 0000 . 1111 0111
201.0.0.247

## Slide 16: Subnetting Example
Forwarding table at router R1
Subnet Number Subnet Mask Next Hop
128.96.34.0 255.255.255.128 interface 0
128.96.34.128 255.255.255.128 interface 1
128.96.33.0 255.255.255.0 R2
All hosts have
address && mask = subnet address
Subnet mask: 255.255.255.128
Subnet number: 128.96.34.0
128.96.34.15
128.96.34.1
H1
R1
128.96.34.130
Subnet mask: 255.255.255.128
Subnet number: 128.96.34.128
128.96.34.129
128.96.34.139
R2
H2
128.96.33.1
128.96.33.14
Subnet mask: 255.255.255.0
Subnet number: 128.96.33.0
H3

## Slide 17: Forwarding Algorithm
D = destination IP address
for each entry (SubnetNum, SubnetMask, NextHop)
D1 = SubnetMask & D
if D1 = SubnetNum
if NextHop is an interface
deliver datagram directly to D
else
deliver datagram to NextHop
Comparisons in parallel, taking the longest match
Use a default router if nothing matches
Not necessary for 1s in subnet mask to be contiguous
Can put multiple subnets on one physical network

## Slide 18: Example
Problem: Your company has bought IP 96.0.0.0 from IANA. Your manager asks you to design the network such that no subnet wok should exceed more than 68 nodes.
• What will be the subnet mask
What is the first IP address of the first, second and last subnet
What is the last IP address of the first, second and last subnet
Also write the broadcast address of the first, second and last subnet

## Slide 19: Example
Solution: IP=96. 0 . 0 . 0
0110 0000. 0000 0000 . 0000 0000 . 0000 0000
96 => Class A IP Address = > 8 Network Bits and 24 Host Bits
No_of_bits_for_hosts = 7
Subnet Mask = 1111 1111 . 1111 1111 . 1111 1111 . 1000 0000
255.255.255.128

## Slide 20: Example
First Subnet:
Subnet Address:
0110 0000. 0000 0000 . 0000 0000 . 1000 0000
96.0.0.128
First IP:
0110 0000. 0000 0000 . 0000 0000 . 1000 0001
96.0.0.129
Last IP:
0110 0000. 0000 0000 . 0000 0000 . 1111 1110
96.0.0.254
Broadcast Address:
0110 0000. 0000 0000 . 0000 0000 . 1111 1111
96.0.0.255

## Slide 21: Example
Second Subnet:
Subnet Address:
0110 0000. 0000 0000 . 0000 0001. 0000 0000
96.0.1.0
First IP:
0110 0000. 0000 0000 . 0000 0001 . 0000 0001
96.0.1.1
Last IP:
0110 0000. 0000 0000 . 0000 0001 . 0111 1110
96.0.1.126
Broadcast Address:
0110 0000. 0000 0000 . 0000 0001 . 0111 1111
96.0.1.127

## Slide 22: Example
Last Subnet:
Subnet Address:
0110 0000. 1111 1111 . 1111 1111 . 0000 0000
96.255.255.0
First IP:
0110 0000. 1111 1111 . 1111 1111 . 0000 0001
96.255.255.1
Last IP:
0110 0000. 1111 1111 . 1111 1111 . 0111 1110
96.255.255.126
Broadcast Address:
0110 0000. 1111 1111 . 1111 1111 . 0111 1111
96.255.255.127

## Slide 23: Subnetting
Subnets allow hierarchy within organizations
But do not reduce class B address pressure

## Slide 24: Supernetting
A supernet is created by combining several Internet Protocol (IP) networks or subnets into one network with a single classless interdomain routing (CIDR) prefix.
The procedure used to create a supernet is commonly called supernetting, route aggregation or route summarization.
Supernetting, also called Classless Inter-Domain Routing (CIDR), is a way to aggregate multiple Internet addresses of the same class.

## Slide 25: Supernetting
Using supernetting, the network address 192.168.2.0/24 and an adjacent address 192.168.3.0/24 can be merged into 192.168.2.0/23.
The "23" at the end of the address says that the first 23 bits are the network part of the address, leaving the remaining nine bits for specific host addresses.
Supernetting is most often used to combine Class C network addresses and is the basis for most routing protocols currently used on the Internet.