## Slide 1: CSC- 362 Computer Networks Week:14 Lecture: 27 - 28
                Prepared by:
                Mr. Attique Ur Rehman

## Slide 2: Transport Layer

## Slide 3: The Big Picture
You are here
Final exam is here

## Slide 4: The Big Picture
today’s topic
application
end-to-end
physical
IP
data link
}
most coverage until now
}

## Slide 5
End-to-end Protocols
Outline
  (reading: Peterson and Davie, Ch. 5)
  End-to-end service model
  Protocol examples
  – User Datagram Protocol (UDP)
  – Transmission Control Protocol (TCP)
    Connection Establishment/Termination
    Sliding Window Revisited
    Flow Control; and adaptive Timeout
  Remote Procedure Call (RPC)

## Slide 6: Where we are now …
Understand how to
  Build a network on one physical medium
  Connect networks together (with switches)
  Implement a reliable byte stream on a variable network (like the Internet)
  Implement a UDP/TCP connection/channel
  Address network heterogeneity
  Address global scale
Today’s topic
  End-to-end issues and common protocols

## Slide 7: End-to-End Service Model
Recall user perspective of network
  Define required functionality/services
  Implementation is irrelevant
Focus of end-to-end protocols (transport layer)
  Communication between applications (users)
  Translating from host-to-host services (network layer)
Services implemented in end-to-end protocols
  Those that cannot be done well in lower layers (i.e., on a per-hop basis); duplicate effort should be avoided
  Those not needed by all applications

## Slide 8: End-to-End Service Model
Services provided by underlying network: IP - “best effort” delivery
  Messages sent from a host, delivered to a host (no distinction between entities sharing a host)
  Drops some messages
  Reorders messages
  Delivers duplicate copies of a message
  Limits messages to some finite size
  Delivers messages after an arbitrarily long delay

## Slide 9: End-to-End Service Model
Common end-to-end services demanded by applications
  Multiple connections (application processes) per host
  Guaranteed message delivery
  Messages delivered in the order they are sent
  Messages delivered at most once
  Arbitrarily large message support
  Synchronization between sender and receiver
  Flow control by the receiver

## Slide 10: End-to-End Protocol Challenge
Given IP service model
Provide service model demanded by applications
Service models to consider
  Demultiplexing only (UDP)
  Everything on the previous list (TCP)
  Reliable request/response (RPC)
https://enterprise.netscout.com/edge/tech-tips/difference-between-tcp-and-udp
https://www.diffen.com/difference/TCP_vs_UDP
https://www.geeksforgeeks.org/differences-between-tcp-and-udp/

## Slide 11: Difference Between TCP and UDP
TCP | UDP
Reliable | Unreliable
Connection-oriented | Connectionless
Segment retransmission and flow control through windowing | No windowing or retransmission
Segment sequencing | No sequencing
Acknowledge sequencing | No acknowledgment

## Slide 12: User Datagram Protocol (UDP)
Thin veneer over IP services
Addresses multiplexing of multiple connections
Unreliable and unordered datagram service
No flow control
Endpoints identified by ports (multiplexing)
  16-bit port space
  Well-known ports for certain services (see /etc/services)
Checksum to validate header
  Optional in IPv4, but mandatory in IPv6 (why ?)

## Slide 13: UDP Header Format
Length includes 8-byte header and data
Checksum (purpose ?)
  Uses IP checksum algorithm
  Computed on pseudo-header, UDP header and data
source port
destination port
UDP length
UDP checksum
0
16
31
source IP address
destination IP address
0
16
31
0
UDP length
17 (UDP)
8

## Slide 14: Reliable Byte-Stream (TCP)
Outline
  Connection Establishment/Termination
  Sliding Window Revisited
  Flow Control
  Adaptive Timeout

## Slide 15: Transmission Control Protocol (TCP)
Service model implements requirements listed earlier
  Multiple connections per host
  Guaranteed and in-order delivery
  Messages delivered at most once
  Arbitrarily large messages
  Synchronization between sender and receiver
  Flow control
Multiplexing mechanism equivalent to that of UDP
Checksum mechanism also equivalent, but mandatory

## Slide 16: TCP Overview
Flow control: restricts rate to something manageable by receiver
Congestion control: restricts rate to something manageable by network
Connection-oriented: setup and teardown required
Full duplex
  Data flows in both directions simultaneously
  Point-to-point communication
Byte stream abstraction: no boundaries in data

## Slide 17: TCP Byte Stream
Application writes bytes
TCP sends segments
Application reads bytes
Application process
W
rite
bytes
TCP
Send buffer
Segment
Segment
Segment
T
ransmit segments
Application process
Read
bytes
TCP
Receive buffer
…
…
…

## Slide 18: Data Link versus Transport
Potentially connects many different hosts
  Need explicit connection establishment and termination
Potentially different RTT
  Need adaptive timeout mechanism
Potentially long delay in network
  Need to be prepared for arrival of very old packets
Potentially different capacity at destination
  Need to accommodate different node capacity
Potentially different network capacity
  Need to be prepared for network congestion

## Slide 19: TCP Outline
TCP vs. a sliding window on a direct link
Model of use
Segment header format and options
States and state diagram (think-pair-share)
Sliding window implementation details
Flow control issues
Bit allocation limitations
Adaptive retransmission algorithms

## Slide 20: TCP vs. Sliding Window on Direct Link
RTT varies
  Among peers (hosts at other end of connections)
  Over time
  Requires adaptive approach to retransmission (and window sizes)
Packets can be
  Delayed for long periods (assume 60 seconds)
  Reordered in the network
  Must be prepared for arrival of very old packets

## Slide 21: TCP vs. Sliding Window on Direct Link
Peer capabilities vary
  Minimum link speed on route
  Buffering capacity at destination
  Requires adaptive approach to window sizes
Network capacity varies
  Other traffic competes for most links
  Requires (global) congestion control strategy
Why not implement more functionality in IP, e.g., ordering guarantees or congestion control ?

## Slide 22: End-to-End Argument
A function should not be provided at a given layer unless it can be completely and correctly implemented at that layer
In-order delivery: hop-by-hop ordering guarantee is not robust to path changes or multiple paths
A
B
C
D
E
F

## Slide 23: End-to-End Argument
Congestion control
  Should be stopped at source
  But network can provide feedback
A
B
C
D
E
F
100Mbps
100Mbps
10Mbps
10Mbps
1Mbps
100Mbps
5Mbps
1Mbps
100Mbps
5Mbps
10Mbps
blue should get 9Mbps, but gets only 5Mbps with hop-by-hop drops

## Slide 24: TCP Model of Use
Connection setup via 3-way handshake
Data transport
  Sender writes some data
  TCP
    Breaks data into segments
    Sends each segment over IP
    Retransmits, reorders, and removes duplicates as necessary
  Receiver reads some data
Teardown through 4-step exchange

## Slide 25: TCP Connection Setup
TCP Connection Setup via 3-way Handshake
  J and K are (different) sequence numbers for messages
  Sequence numbers need not start at zero
Active participant
(client)
Passive participant
(server)
SYN J
SYN K
ACK J+1
ACK K+1

## Slide 26: TCP Data Transport Model
Data broken into segments
  Limited by maximum segment size (MSS)
  Defaults to 536 bytes
  Negotiable during connection setup
  Typically set to MTU of directly connected network minus size of IP and TCP headers (40 bytes)
Three events send segment
  >= MSS bytes of data ready to be sent
  Explicit PUSH operation by application
  Periodic timeout

## Slide 27: TCP Connection Teardown
TCP connection teardown in 4 steps
  Either client or server can initiate connection teardown
  FIN is associated with sequence number space (why?)
client
server
FIN J
FIN K
ACK K+1
ACK J+1
active close
passive close
closes connection

## Slide 28: TCP Segment Header & Pseudo-Header
source port
destination port
sequence number
0
16
31
ACK sequence number
hdrlen
advertised window
0
flags
TCP checksum
urgent pointer
options (variable)
4
10
source IP address
destination IP address
0
16
31
0
TCP length
6 (TCP)
8

## Slide 29: TCP Segment Header
16-bit source and destination ports
32-bit send and ACK sequence numbers
4-bit header length in 4-byte words (minimum 5)
Six 1-bit flags
  URG: segment contains urgent data
  ACK: ACK sequence number is valid
  PSH: do not delay delivery of data
  RST: reset connection (rejection or abnormal termination); no sequence number associated
  SYN: synchronize segment for setup
  FIN: final segment for teardown

## Slide 30: TCP Segment Header
16-bit advertised window
  Space remaining in receive window
16-bit checksum
  Uses IP checksum algorithm
  Computed on header, data, and pseudo-header
16-bit urgent data pointer
  If URG=1
  Index of last byte of urgent data in segment

## Slide 31: TCP Segment Format
Each connection identified with 4-tuple:
  (SrcPort,SrcIPAddr,DsrPort,DstIPAddr)
Sliding window + flow control
  ACK, SequenceNum, AdvertisedWindow
Flags
  SYN, FIN, RESET, PUSH, URG, ACK
Sender
Data
(SequenceNum)
Acknowledgment +
AdvertisedWindow
Receiver

## Slide 32: TCP Options – Existing & Proposed
Negotiate maximum segment size (MSS)
  Each host suggests a value
  Minimum of two values is chosen
  Prevents IP fragmentation over first/last hops
Packet timestamp
  Allows RTT calculation for retransmitted packets
  Extends sequence number space for identification of stray packets (packets arriving very late)
Negotiate advertised window granularity
  Allows larger windows
  Good for routes with large bandwidth-delay products

## Slide 33: TCP State Description
CLOSED disconnected
LISTEN waiting for incoming connection
SYN_RCVD connection request received
SYN_SENT connection request sent
ESTABLISHED ready for data transport
CLOSE_WAIT connection closed by peer
LAST_ACK closed by peer, closed locally, await ACK
FIN_WAIT_1 connection closed locally
FIN_WAIT_2 closed locally and ACK’d
CLOSING closed by both sides “simultaneously”
TIME_WAIT wait for network to discard related packets

## Slide 34: State Transition Diagram
CLOSED
LISTEN
SYN_RCVD
SYN_SENT
ESTABLISHED
CLOSE_WAIT
LAST_ACK
CLOSING
TIME_WAIT
FIN_WAIT_2
FIN_WAIT_1
Passive open
Close
Send/
SYN
SYN/SYN + ACK
SYN + ACK/ACK
SYN/SYN + ACK
ACK
Close
/FIN
FIN/ACK
Close
/FIN
FIN/ACK
ACK + FIN/ACK
Timeout after two segment lifetimes
FIN/ACK
ACK
ACK
ACK
Close
/FIN
Close
CLOSED
Active open
/SYN

## Slide 35: Think-Pair-Share
Describe the path taken
  By a server under normal conditions, and
  By a client under normal conditions,
  Assuming that the client closes the connection first.
Consider the TIME_WAIT state
  What purpose does this state serve ?
  Prove that at least one side of a connection enters this state before returning to CLOSED
  Explain how both sides might enter this state

## Slide 36: Sliding Window Implementation
Sequence numbers are indices into byte stream
ACK sequence number is actually next byte expected (as opposed to last byte received)
Receiver buffers contain
  Data ready for delivery to application until requested
  Out-of-order data out to maximum buffer capacity
Sender buffers contain
  Unacknowledged data
  Unsent data out to maximum buffer capacity

## Slide 37: Sliding Window
Sender side
  Green: sent and acknowledged
  Red: sent (or can be sent) but not acknowledged
  Blue: available but not within send window
time
LastByteAcked
LastByteSent
LastByteWritten
application
TCP
Window
max buffer size

## Slide 38: Sliding Window
Receiver side
  Green: received and ready to be delivered
  Red: received and buffered
  Blue: received and discarded
time
NextByteRead
NextByteExpected
LastByteReceived
application
TCP
Advertised window
max buffer size

## Slide 39: Flow vs. Congestion Control
Flow control prevents buffer overflow at receiver (only source and dest. are relevant)
Congestion control addresses bandwidth interactions between distinct packet flows
TCP provides both
  flow control based on advertised window
  congestion control will be discussed later …

## Slide 40: TCP Flow Control Issues
Problem: slow receiver application
  Advertised window goes to 0
  Sender cannot send more data
  Non-data packets used to update window ?
  Receiver may not spontaneously generate, or update may be lost
Solution: smart sender/dumb receiver
  Sender periodically sends a 1-byte segment, ignoring advertised window of 0
  Eventually, window opens
  Sender learns of opening from next ACK of 1-byte segment

## Slide 41: TCP Flow Control Issues
Problem: app. delivers tiny pieces of data to TCP
  e.g., telnet in character mode
  Each piece sent as segment, returned as ACK
  Very inefficient
Solutions
  Delay transmission to accumulate more data
  Nagle’s algorithm
    Send first piece
    Accumulate data until first piece ACK’d
    Send accumulated data and restart accumulation
    Not ideal for some traffic, e.g., mouse motion

## Slide 42: TCP Flow Control Issues
Problem: slow application reads data in tiny pieces
  Receiver advertises tiny window
  Sender fills tiny window
  Known as silly window syndrome
Solution: due to Clark
  Advertise window opening only when MSS or ½ of buffer is available
  Sender delays sending until window is MSS or ½ of receiver’s buffer (estimated)
  Overridden by using PUSH