## Slide 1: CSC- 362 Computer Networks Week:15 Lecture:19 - 20
                Prepared by:
                Mr. Attique Ur Rehman

## Slide 2: Application Layer

## Slide 3: The Big Picture
You are almost here
Final exam is here

## Slide 4
Application Layer
Outline
  Application Layer Protocols

## Slide 5: Where we are now …
Understand how to
  Build a network on one physical medium
  Connect networks together (with switches)
  Implement a reliable byte stream on Internet
  Implement a UDP/TCP connection/channel
  Address network heterogeneity
  Address global scale
  End-to-end issues and common protocols
  Congestion control and resource allocation
Today’s topic
  Applications, with focus on their protocols

## Slide 6: Application Layer Protocol
Networking support:
  Domain Name System (DNS)
File transfer:
  File Transfer Protocol (FTP)
  Trivial File Transfer Protocol (TFTP)
Remote login to hosts:
  Telnet
Electronic mail transport:
  Simple Mail Transfer Protocol (SMTP)
  Multipurpose Internet Mail Extensions (MIME)

## Slide 7: Application Layer Protocol
Host initialization:
  BOOTP
Remote host management:
  Simple Network Management Protocol (SNMP)
  Common Management Information Protocol over TCP (CMOT)

## Slide 8: Domain Name Service (DNS)
Translates Internet domain names into IP addresses
Example of a distributed application
Defined in RFC’s 1034 and 1035
DNS Outline
  Comparison of domain names and addresses
  Domain name hierarchy
  Implementation of hierarchy
  Name resolution (name to address translation)

## Slide 9: Domain Names and Addresses
Internet domain names: human readable
  Mnemonic of variable length
  e.g., donald2.inria.fr
IP addresses: easily handled by routers/computers
  Fixed length string tied (loosely) to geography
  e.g., 131.126.143.82
Levels of hierarchy
  Each capable of arbitrary number
  AS implements beyond two levels

## Slide 10: Domain Name Hierarchy
Structure: period-separated identifiers
  Host name first
  Each subsequent component is larger group
  Little-endian ?
org
com
edu
net
gov
mil
pk
fr
ietf
ibm
yahoo
mit
uiuc
edu
inria
www
cs
ee
case
cupidon
research

## Slide 11: Domain Name Hierarchy
Each identifier (after host name) denotes a zone
Translation for each zone supported by 2+ name servers
org
com
edu
net
gov
mil
pk
fr
ietf
ibm
yahoo
mit
uiuc
edu
inria
www
cs
ee
case
cupidon
research
Example zones

## Slide 12: Domain Name Service
Name servers maintain
  Collection of resource records (5-tuples: name, value, type, class, TTL)
Each record is a translation based on type
  Type=A: name=full domain name, value=IP addr.
  Type=NS: name=subzone name, value=subzone name server’s full domain name
  Type=CNAME: name=domain name alias, value=canonical domain name for host
  Type=MX: name=zone name, value=maildrop host’s full domain name

## Slide 13: Domain Name Service
Resource record tuple format: (name, value, type, class, TTL)
Class
  Generally set to IN (Internet)
  Allows use of DNS for other purposes
  Not often used, however
TTL (time to live)
  Guarantee on translation validity
  Used for caching; discard copy on timeout

## Slide 14: Examples of Resource Records
Root name server: (<name, value, type, class>)
<arizona.edu, telcom.arizona.edu, NS, IN >
<telcom.arizona.edu, 128.196.128.233, A, IN >
< bellcore.com, thumper.bellcore.com, NS, IN >
< thumper.bellcore.com, 128.96.32.20, A, IN >

## Slide 15: Examples of Resource Records
Arizona’s name server: (<name, value, type, class>)
<cs.arizona.edu, optima.cs.arizona.edu, NS, IN>
<optima.cs.arizona.edu, 192.12.69.5, A, IN>
<ece.arizona.edu, helios.ece.arizona.edu, NS, IN>
<helios.ece.arizona.edu, 128.196.28.166, A, IN>
<jupiter.physics.arizona.edu, 128.196.4.1, A, IN>
<saturn.physics.arizona.edu, 128.196.4.2, A, IN>

## Slide 16: Examples of Resource Records
Arizona’s CS name server: (< name, value, type, class>)
<cs.arizona.edu, optima.cs.arizona.edu, MX, IN>
<optima.cs.arizona.edu, 192.12.69.5, A, IN >
<opt.cs.arizona.edu, optima.cs.arizona.edu, CNAME, IN >

## Slide 17: Name Resolution Example
client
local name server
.edu root name server
UIUC name server
ECE name server
www.ece.uiuc.edu
www.ece.uiuc.edu
uiuc.edu; 131.126.10.23
www.ece.uiuc.edu
ece.uiuc.edu; 131.126.150.1
www.ece.uiuc.edu
www.ece.uiuc.edu; 131.126.150.25
131.126.150.25

## Slide 18: Traditional Applications
Directly invoked by users
Employ the request/reply paradigm
  Own RPC-like mechanism on top of TCP/UDP
Distinction between application programs and application protocols
  E.g. web browser and HTTP
Companion protocols specifying data format
  E.g. MIME with SMTP, HTML with HTTP, etc.

## Slide 19: Electronic Mail
One of the most successful application of the Internet
Understanding how email works requires to distinguish
  The user interface from underlying message transfer protocol, i.e. mail reader from SMTP
  The transfer protocol and a companion protocol that defines format of messages being exchanged, i.e. SMTP from RFC 822 + MIME

## Slide 20: RFC 822 Message Format
Message have two parts: header and body
  Both parts are represented in ASCII text
  Header is separated from the message body by a blank line
Message header is a series of lines containing type and value separated by a colon
  Some fields are filled by user (e.g. To: ), other are filled by the mail delivery system (e.g. Date: )
RFC 822 explains all header fields …

## Slide 21: Format of an Email

## Slide 22: Email Address

## Slide 23: User Agent
Some examples of command-driven user agents are mail, pine, and elm
Some examples of GUI-based user agents are Eudora, Outlook, and Netscape

## Slide 24: Multipurpose Internet Mail Extensions (MIME)
RFC 822 was extended to allow email messages to carry many different types of data: audio, images, documents, …
Mime consists of three basic pieces
The first piece is a collection of header lines that augment the original set defined by RFC 822
  Describe the data being carried in the message body
  E.g. content-type, content-transfer-encoding, etc.

## Slide 25: MIME
Second piece is definitions for a set of content types and sub-types
  image/gif, image/jpeg
  text/plain, text/richtext (marked up text with fonts, etc.)
  application/postscript, application/msword
“Multipart” type defines how message carrying different data types is structured
  Each piece has its own header line describing the type

## Slide 26: MIME
Third piece is a way to encode various data types
  After encoding, whole message is an ASCII text
  Message passes through a number of gateways that assume all email is ASCII
MIME uses base64 encoding of binary data into the ASCII character set
  Map every three bytes of original binary data into four ASCII characters
  Grouping data into 24-bit pieces, then to four 6-bit pieces which maps to one of 64 valid ASCII characters

## Slide 27: MIME

## Slide 28: MIME Header

## Slide 29: Data Types and Sub-types in MIME
Type | Subtype | Description
Text | Plain | Unformatted text
Multipart | Mixed | Body contains ordered parts of different data types
 | Parallel | Same as above, but no order
 | Digest | Similar to mixed, but the default is message/RFC822
 | Alternative | Parts are different versions of the same message
Message | RFC822 | Body is an encapsulated message
 | Partial | Body is a fragment of a bigger message
 | Ext. Body | Body is a reference to another message
Image | JPEG | Image is in JPEG
 | GIF | Video is in GIF format
Video | MPEG | Video is in MPEG format
Audio | Basic | Single-channel encoding of voice at 8 KHz
Application | PostScript | Adobe PostScript
 | Octet-Stream | General binary data (8-bit bytes)

## Slide 30: Content-transfer Encoding
Category | Description
Type | ASCII characters and short lines
7bit | Non-ASCII characters and short lines
8bit | Non-ASCII characters with unlimited-length lines
Binary | 6-bit blocks of data are encoded into 8-bit ASCII characters
Base64 | Non-ASCII characters are encoded as an equal sign followed by an ASCII code

## Slide 31: Base 64

## Slide 32: Base 64 Encoding Table
Value | Code | Value | Code | Value | Code | Value | Code | Value | Code | Value | Code
0 | A | 11 | L | 22 | W | 33 | h | 44 | s | 55 | 3
1 | B | 12 | M | 23 | X | 34 | i | 45 | t | 56 | 4
2 | C | 13 | N | 24 | Y | 35 | j | 46 | u | 57 | 5
3 | D | 14 | O | 25 | Z | 36 | k | 47 | v | 58 | 6
4 | E | 15 | P | 26 | a | 37 | l | 48 | w | 59 | 7
5 | F | 16 | Q | 27 | b | 38 | m | 49 | x | 60 | 8
6 | G | 17 | R | 28 | c | 39 | n | 50 | y | 61 | 9
7 | H | 18 | S | 29 | d | 40 | o | 51 | z | 62 | +
8 | I | 19 | T | 30 | e | 41 | p | 52 | 0 | 63 | /
9 | J | 20 | U | 31 | f | 42 | q | 53 | 1 |  | 
10 | K | 21 | V | 32 | g | 43 | r | 54 | 2 |  | 

## Slide 33: Quoted-printable

## Slide 34: Message Transfer – SMTP
Users interact with a mail reader
Mail daemon (or process) running on each host playing the role of a post office
Mail reader gives message to mail daemon
Mail daemon used SMTP (running on TCP) to transmit message to a daemon on another machine
Daemon puts incoming message into user mailbox
Mail reader can read the message later

## Slide 35: Mail Transfer – SMTP
SMTP implementations are derived from sendmail
Often the mail traverses one or more mail gateways on its route from sender to receiver
Mail gateways also run a sendmail process and store and forward email messages
Mail gateways buffers messages on disk and try retransmitting them to the next machine for several days

## Slide 36: Mail Gateways
Why are mail gateways necessary?
  Recipient does not want to include his host’s name in his email address
  Recipient’s machine may not always be up
Independent SMTP connection between mail gateways (and hosts)
  Multiple messages may be transferred in single session
SMTP client posts a command and the server responds with a code

## Slide 37: MTA Client and Server

## Slide 38: MTA – Commands and Responses

## Slide 39: Email Delivery

## Slide 40: Mail Reader and Mail Access Protocol
User performs all actions by interacting with the mail reader
  E.g. retrieves its mail from the mailbox at the server
Mail reader uses mail access protocol to retrieve messages from the server
  Internet Message Access Protocol (IMAP)
  Post Office Protocol (POP)

## Slide 41: POP3

## Slide 42: World Wide Web (HTTP)
Very successful application of the Internet
Set of cooperating clients and servers, speaking the same language: HTTP
Graphical client program (web browser) displays a page of information
Browser allows the user to open a URL (Uniform Resource Locator): location of object on the web
Browser opens a TCP connection (on the well-known port 80) to web servers

## Slide 43: World Wide Web (HTTP)
Files on the web contain text, images, …
Also include URLs that point to other files
  Embedded URLs are called hypertext links
Embedded URLs may be followed by opening a new connection to retrieve and display the object
Object fetched using text-oriented protocol HTTP
  Request/response messages with options and parameters

## Slide 44: HTTP Transaction

## Slide 45: Request Message

## Slide 46: Request Line
HTTP request message specifies operation to be performed, web page the operation should be performed on, and the HTTP version
E.g. GET http://www.case.edu.pk HTTP/1.1

## Slide 47: Response Message

## Slide 48: Status Line
Response message begins with the status line specifying the version of HTTP, 3-digit code indicating success or not, and the text string giving the reason
E.g. HTTP/1.1 202 Accepted

## Slide 49: Headers and Header Format

## Slide 50: HTTP Example 1

## Slide 51: HTTP Example 2

## Slide 52: Distributed Services

## Slide 53: HTTP and TCP Connections
HTTP 1.0 establishes a separate TCP connection for each data item retrieved
  Inefficient mechanism with connection setup/teardown
HTTP 1.1 allows persistent connections
  Client and server exchange multiple request/response messages over the same TCP connection
  Reduced load on server, lesser delay, etc.
With persistent connections, neither the client nor the server knows how long to keep the connection open

## Slide 54: Browser Architecture

## Slide 55: Hypertext

## Slide 56: Static Document

## Slide 57: Dynamic Document

## Slide 58: Active Document

## Slide 59: Streaming Stored Audio/Video: Using a Web Server

## Slide 60: Streaming Stored Audio/Video: Using a Web Server with a Metafile

## Slide 61: Streaming Stored Audio/Video: Using a Media Server

## Slide 62: Streaming Stored Audio/Video: Using a Media Server and RTSP

## Slide 63: Real-time Transport Protocol (RTP)
Application-Level Framing
Data Packets
  sequence number
  timestamp (app defines “tick”)
Control Packets (send periodically)
  loss rate (fraction of packets received since last report)
  measured jitter

## Slide 64: Time Relationship

## Slide 65: Jitter
Jitter is introduced in real time data by the delay between packets

## Slide 66: Timestamps

## Slide 67: Playback Buffer
To prevent jitter, we can timestamp the packets and separate arrival time from the playback time

## Slide 68: Real-time Traffic Issues
A playback buffer is required for real-time traffic
A sequence number on each packet is required for real-time traffic
Real-time traffic needs the support of multicasting
Mixing means combining several streams of traffic into one stream

## Slide 69: Transport Protocol for RTP
TCP, with all its sophistication, is not suitable for interactive multimedia traffic because we cannot allow retransmission of packets
UDP is more suitable than TCP for interactive traffic. However, we need the services of RTP, another transport layer protocol, to make up for the deficiencies of UDP

## Slide 70: Transport Protocol for RTP
RTP uses a temporary even-numbered UDP port
RTCP uses an odd-numbered UDP port number that follows the port number selected for RTP

## Slide 71: RTCP Message Types

## Slide 72: Overlay Network Layered on Top of a Physical Network

## Slide 73: Overlay Nodes Tunnel Through Physical Nodes

## Slide 74: Multicast Trees Mapped Onto a Physical Topology

## Slide 75: Multicast Tree Embedded in an Overlay Mesh