## Slide 1: CSC- 362 Computer Networks Week:16 Lecture: 21-22
                Prepared by:
                Mr. Attique Ur Rehman

## Slide 2: Network Security

## Slide 3: The Big Picture
You are almost here
Final exam is here

## Slide 4
Network Security
Outline
  Network Security

## Slide 5: Triangular Inequality in Networks

## Slide 6: Denial of Service Attacks
Denial of service attacks crippled e-commerce and various major Internet-based companies ! (News)
What is denial of service?
How does it traditionally work?
  IP spoofing example
  Key elements
What’s new about the recent attacks?
What has changed to make the new attacks possible?

## Slide 7: What is Denial of Service ?
Denial of service is
  A malicious attack
  Based on the concept of overloading
  Components along the route to a server
  Or the server itself
Due to the increased workload, the overloaded component responds slowly or not at all to legitimate requests
Consider the following …

## Slide 8: What is Denial of Service ?
This slide is intended to demonstrate the concept of denial of service by placing useful information in the middle of a paragraph of drivel. If you’ve gotten this far, you may want to jump to the middle or scan around, but you’re unlikely to find the important part before I skip to the next slide, simulating the fact that the garbage doesn’t stop coming in a denial of service attack. In fact, in some cases you may get nothing but garbage. If you recall how IP datagram services work, for example, then you can reason about the likelihood of legitimate requests spaced by increasingly long TCP timeouts finding an empty queue slot in a router fed from another input by a continuous stream of bogus packets. When a slot opens up, it is quickly grabbed by the next bogus packets and rarely available for the real thing.

## Slide 9: What is Denial of Service ?
So did you get the point ?
read
During a denial of service attack, do servers continue to receive client requests?

## Slide 10: What is Denial of Service ?
This slide is intended to demonstrate the concept of denial of service by placing useful information in the middle of a paragraph of drivel. If you’ve gotten this far, you may want to jump to the middle or scan around, but you’re unlikely to find the important part before I skip to the next slide, simulating the fact that the garbage doesn’t stop coming in a denial of service attack. In fact, in some cases you may get nothing but garbage. If you recall how IP datagram services work, for example, then you can reason about the likelihood of legitimate requests spaced by increasingly long TCP timeouts finding an empty queue slot in a router fed from another input by a continuous stream of bogus packets. When a slot opens up, it is quickly grabbed by the next bogus packets and rarely available for the real thing.

## Slide 11: How Does It Traditionally Work ?
Example: IP spoofing
Remember the TCP SYN segment ?
  Client sends SYN to server
  Server reserves queue entry
  Server sends back SYN.
Server sends back SYN to where?
  Client IP must be included in first SYN
  What if the client lies ? “Hi, please contact Prof. ABC’s computer”

## Slide 12: IP Spoofing
Pretending to be Prof. ABC’s computer
  It responds
  Queue resources freed up
  Not terribly effective
Instead, pick a computer that probably won’t respond
  A random number works nicely
  Return SYN gets lost
  Server waits 75 seconds before freeing queue entry

## Slide 13: What are the Key Elements ?
Expansion in required work
  Easy for me, hard for you
  In spoofing
    Creating and sending a SYN: a few microseconds
    Timing out a queue entry: 75 seconds
  protocols that admit starvation
    IP routers
      Drop datagrams when output buffer full
      Independent of source input
  Result is that clients can be starved
  Painfully slow even without starvation

## Slide 14: What’s New About the Recent Attacks ?
Expansion factor allows attack by a few or one
Alternative
  Attack by many
  Requires many resources distributed across Internet
  Benefits from expansion, too
Attack software
  Probably installed indirectly
  Apparently resident for some time
  No significant trail remains

## Slide 15: What Changed to Make Attacks Possible ?
Change of Internet character
  Many more machines
  Many more naive users
  Much more complex software
Old internet
  Very little interpretation of data (e.g., e-mail)
  Operating system bugs relative secure (by obscurity)
  Security-savvy administrator required (so security breaches detected and repaired)

## Slide 16: What Changed to Make Attacks Possible ?
New Internet
  Point-and-click network installation
  Very broad interfaces
  Even transparent code encapsulation
  And self-installing “plug-ins”!
  Public source operating systems, too
  (And frustrated security gurus writing tools to eliminate any remaining obscurity)

## Slide 17: What Changed to Make Attacks Possible ?
Example of attack:
  Abuse bug in Internet Explorer to install flashing window telling owner to download patch
  What else might someone install instead?

## Slide 18: IP Spoofing Countermeasures
IP spoofing
  Abuses TCP connection queue time expansion
  Considered unsolvable for quite some time
  Solved by ingenious use of cryptography
Solution
  Return one-use key with response SYN segment
  Reserve no queue resources
  ACK to second SYN (third step of setup) must return the key
  IP spoofing never sends such an ACK