## Slide 1: CSC- 362 Computer Networks Week-4 Lecture- 7-8
                Prepared by:
                Mr. Attique Ur Rehman

## Slide 2: Instructor Contact Details
Name: Mr. Attique Ur Rehman
Course Instructor: CSC362- Computer Networks
Credit Hours: (3+1)=4
Office Location: 2nd Floor Computer Science Faculty Office: 41-C
Email: attique.rehman@lgu.edu.pk
Visiting Hours: Wednesday (11:30 am -1:00 pm)

## Slide 3: Course Material
Reference books
  Many textbooks on Networking may be consulted
Research papers!
RFCs and Internet drafts
  Related to TCP/IP suite and other protocols
Web resources
  Tutorials, white papers, reports, etc.

## Slide 4: Text Book
Computer Networks: A Systems Approach by Larry L. Peterson and Bruce S. Davies.
  Third Edition [2003], Morgan Kaufmann Publishers, San Mateo, California, USA
Computer Networks by Andrew S. Tanenbaum
    Fifth Edition
Data Communication and Computer Networks, by Behrouz A. Forouzan
    5th Edition
Data and Computer Communications by William Stallings
  10th Edition
Computer Networking: A Top-Down Approach Featuring the Internet by James F. Kurose and Keith W. Ross
  6th edition

## Slide 5: Error Detection or Correction ?
Data can corrupted during transmission
Some applications require that errors be detected and corrected.
Detection implies discarding message and waiting for retransmission
  uses bandwidth
  introduces latency
Error correction requires more redundant bits to send all the time : error-correcting code (FEC)‏
Error correction is useful when:
  errors are quite probable (wireless links)‏
  retransmission cost is too high (latency in satellite link, multicast)‏

## Slide 6: Types of Error
Single bit error
  only 1 bit in the data unit has changed.
Burst Error
  2 or more bits in data units have changed

## Slide 7: Error Detection or Correction: Structure of Sender and Receiver
To detect or correct errors, we need to send extra (redundant) bits with data.

## Slide 8: Error Detection
Why we need it ?
  To avoid retransmission of whole packet or message
What to do if error detected ?
  Discard, and request a new copy of the frame:
    explicitly or implicitly
  Try to correct error, if possible

## Slide 9: Error Detection
Validates correctness of each frame
Errors checked at many levels
Demodulation of signals into symbols (analog)‏
Bit error detection/correction (digital)—our main focus
  Within network adapter (CRC check)‏
  Within IP layer (IP checksum)‏
  Possibly within application as well

## Slide 10: Error Detection: How ?
How to detect error ?
  Add redundant information to a frame to determine errors
Transmit two complete copies of data
  n redundant bits for n-bit message
  Error at the same position in two copies go undetected

## Slide 11: Error Detection: How ?
We want only k redundant bits for an n-bit message, where k < < n
  In Ethernet, 32-bit CRC for 12,000 bits (1500 bytes)‏
k bits are derived from the original message
Both the sender and receiver know the algorithm

## Slide 12: Error Correction
Error-correcting codes try to add enough redundant information so that the receiver can still figure out the data if the frame is damaged. This is sometimes referred to as forward error correction.
The overhead is high but it reduces the need to resend frames.
These redundant codes are best suited for networks with high error (wireless).
Notes: 12

## Slide 13: Hamming Distance
The Hamming distance between two words is the number of differences between corresponding bits.
To find hamming distance between two words just XOR them and then count the number of 1 bits in the result.
The Hamming distance d(000, 011) is 2 because
The Hamming distance d(10101, 11110) is 3 because
Notes: 13

## Slide 14: Hamming Distance
110011000011001
010111001011001
-------------------------
100100001000000
The Hamming Distance is 3.
This means 3 bits would have to “flip” before we would be unable to detect an error.
The minimum Hamming distance is the smallest Hamming distance between all possible pairs in a set of words.
Notes: 14

## Slide 15: Codewords
We do not make use of all of the possible codewords due to the use of check bits.
This means we can compute all of the legal codewords and determine the minimum Hamming distance for the set.
In order to detect d errors, we need a distance of d+1.
In order to correct d errors, we need a distance of 2d+1.
Notes: 15

## Slide 16: The Parity Bit
Consider the parity bit that tells us if the parity of the data is even or odd.
The Hamming Distance would equal 2.
Since it is only one bit, then it is able to identify single errors (if one bit has flipped).
If two bits have flipped, then the parity bit will report the correct parity for the data.
Notes: 16

## Slide 17: 1-bit Error Detection with Parity
Every code has even number of 1’s
000
100
110
010
011
001
101
111
01
00
10
11
Valid codes
Parity encoding: gray dots are invalid and indicate errors
if only 1 bit flips, it can be detected

## Slide 18: 1-bit Error Correction with Voting
Every code is copied three times
000
100
110
010
011
001
101
111
0
1
Valid codes
gray dots correct to “1” blue dots correct to “0”
- if only 1 bit flips, it can be corrected
- even with 2 erasures, bit can be recovered

## Slide 19: Error Bits or Error Burst
Common model of errors
  Probability of error per bit
  Error in each bit independent of others
  Value of incorrect bit independent of others
Burst model
  Probability of back-to-back bit errors
  Error probability dependent on adjacent bits
  Value of errors may have structure
Why assume bursts?
  Appropriate for some media (e.g., Radio)‏
  Faster signaling rate enhances such phenomena

## Slide 20: Digital Error Detection Techniques
Two-dimensional parity
  Detects up to 3-bit errors
  Good for burst errors
Cyclic redundancy check (CRC)‏
  Powerful mathematics
  Tricky in software, simple in hardware
  Used in network adapter

## Slide 21: Two-Dimensional Parity
Adding one extra bit to a 7-bit code to balance 1s
extra parity byte for the entire frame
Catches all 1-, 2- and 3-bit errors and most 4-bit errors
14 redundant bits for a 42-bit message, in the example
1011110
1
1101001
0
0101001
1
1011111
0
0110100
1
0001110
1
1111011
0
Parity
bits
Parity
byte
Data

## Slide 22: Two-Dimensional Parity
0
1
0
0
0
1
1
1
0
1
1
0
0
0
1
1
0
1
1
0
1
1
1
1
0
1
1
0
0
0
0
0
1
0
0
1
0
0
1
1
0
1
1
0
1
1
0
0
1
1
0
1
0
1
0
0
0
1
1
0
1
1

## Slide 23: Cyclic Redundancy Check
Theory
based on finite-field (binary-valued) arithmetic
bit string represented as polynomial
coefficients are binary-valued
divide bit string polynomial by generator polynomial to generate CRC
Practice
bitwise XOR’s

## Slide 24: Cyclic Redundancy Check
Add k bits of redundant data to an n-bit message
  want k << n
  e.g., k = 32 and n = 12,000 (1500 bytes)‏
Represent n-bit message as n-1 degree polynomial
  e.g., MSG=10011010 as M(x) = x7 + x4 + x3 + x1
  Sender and receiver exchange polynomials
Let k be the degree of some agreed-upon divisor/ generator polynomial
  e.g., C(x) = x3 + x2 + 1

## Slide 25: Cyclic Redundancy Check
Transmit polynomial P(x) that is evenly divisible by C(x)
  shift left k bits, i.e., M(x)xk
  add remainder of M(x)xk / C(x) into M(x)xk
Receiver receives polynomial P(x) + E(x)‏
  E(x) = 0 implies no errors
Receiver divides (P(x) + E(x)) by C(x); remainder will be zero ONLY if:
  E(x) was zero (no error), or
  E(x) is exactly divisible by C(x)‏

## Slide 26: CRC Example - Sender
C(x) = x3+x2+1 = 1101  generator
M(x) = x8 + x6 + x5 + x4+1 = 101110001  message
1101 ) 101110001000
1101
1101
1101
00001000
1101
101 remainder
k bits

## Slide 27: CRC Example - Receiver
C(x) = x3+x2+1 = 1101  generator
M(x) = x11+x9+x8+x7+x3+x2+1 = 101110001101  message
1101 ) 101110001101
1101
1101
1101
00001101
1101
0 correct !
remainder bits

## Slide 28: CRC Example - Receiver
C(x) = x3+x2+1 = 1101  generator
M(x) = x11+x9+x8+x7+x3+x2+1 = 101110001101  message
1101 ) 101101001101
1101
1100
1101
1100
1101
1110
1101
111 incorrect !
Two bits are flipped

## Slide 29: CRC Example - Receiver
C(x) = x3+x2+1 = 1101  generator
M(x) = x11+x9+x8+x7+x3+x2+1 = 101110001101  message
1101 ) 101101011101
1101
1100
1101
1101
1101
1101
1101
0 incorrectly correct !!!
Three bits are flipped

## Slide 30: Hamming Distance (1950 Paper)‏
Minimum number of bit flips between code words
  2 flips for parity
  3 flips for voting
n-bit error detection
  No code word changed into another code word
  Requires Hamming distance of n+1
n-bit error correction
  N-bit neighborhood: all code words within n bit flips
  No overlap between n-bit neighborhoods
  Requires Hamming distance of 2n+1

## Slide 31: Hamming Codes (1950 Paper)‏
The following general algorithm generates a single-error correcting (SEC) code for any number of bits.
Number the bits starting from 1: bit 1, 2, 3, 4, 5, etc.
Write the bit numbers in binary. 1, 10, 11, 100, 101, etc.
All bit positions that are powers of two (have only one 1 bit in the binary form of their position) are parity bits.
All other bit positions, with two or more 1 bits in the binary form of their position, are data bits.
Each data bit is included in a unique set of 2 or more parity bits, as determined by the binary form of its bit position.

## Slide 32: Hamming Codes (1950 Paper)‏
  Parity bit 1 covers all bit positions which have the least significant bit set: bit 1 (the parity bit itself), 3, 5, 7, 9, etc.
  Parity bit 2 covers all bit positions which have the second least significant bit set: bit 2 (the parity bit itself), 3, 6, 7, 10, 11, etc.
  Parity bit 4 covers all bit positions which have the third least significant bit set: bits 4–7, 12–15, 20–23, etc.
  Parity bit 8 covers all bit positions which have the fourth least significant bit set: bits 8–15, 24–31, 40–47, etc.
  In general each parity bit covers all bits where the binary AND of the parity position and the bit position is non-zero.

## Slide 33: Hamming Codes (1950 Paper)‏

## Slide 34: Bit position of the data and parity bits
2
6
4
7
5
3
1
001
011
101
111
100
110
010

## Slide 35: Graphical depiction of the 4 data bits and 3 parity bits and which parity bits apply to which data bits

## Slide 36: Error Detection and Correction
1 2 3 4 5 6 7
P1 = D1 XOR D2 XOR D4
P2 = D1 XOR D3 XOR D4
P4 = D2 XOR D3 XOR D4
p1
p2
D1
p4
D2
D3
D5
p1
p2
D1
p3
D2
D3
D4
p1
p2
D1
p4
D2
D3
D4
p1
p2
D1
p3
D2
D3
D4

## Slide 37: Graphical depiction of the 7 data bits and 4 parity bits and which parity bits apply to which data bits

## Slide 38: Bit position of the data and parity bits

## Slide 39: Example of (11,7)‏
7-bit data word "0110101“
Data word with parity “10001100101”
If last bit of data word flip “10001100100”
Checking of parity bit
Correction of Error “10001100101”
7-bit data word "0110101“

## Slide 40: Calculation of Hamming code parity bits

## Slide 41: Hamming(11,7) code 7-bit data word "0110101"

## Slide 42: Checking of parity bits (switched bit highlighted)

## Slide 43: Checking of parity bits (switched bit highlighted)

## Slide 44: Correction of Error