## Slide 1: CSC- 362 Computer Networks Week-5 Lecture-9-10
                Prepared by:
                Mr. Attique Ur Rehman

## Slide 2: Instructor Contact Details
Name: Mr. Attique Ur Rehman
Course Instructor: CSC362- Computer Networks
Credit Hours: (3+1)=4
Office Location: 2nd Floor Computer Science Faculty Office: 41-C
Email: attique.rehman@lgu.edu.pk
Visiting Hours: Wednesday (11:30 am -1:00 pm)

## Slide 3: Course Material
Reference books
  Many textbooks on Networking may be consulted
Research papers!
RFCs and Internet drafts
  Related to TCP/IP suite and other protocols
Web resources
  Tutorials, white papers, reports, etc.

## Slide 4: Text Book
Computer Networks: A Systems Approach by Larry L. Peterson and Bruce S. Davies.
  Third Edition [2003], Morgan Kaufmann Publishers, San Mateo, California, USA
Computer Networks by Andrew S. Tanenbaum
    Fifth Edition
Data Communication and Computer Networks, by Behrouz A. Forouzan
    5th Edition
Data and Computer Communications by William Stallings
  10th Edition
Computer Networking: A Top-Down Approach Featuring the Internet by James F. Kurose and Keith W. Ross
  6th edition

## Slide 5: Reliable Transmission
Higher level of abstraction (transport layer vs. data link layer‏
my
computer’s
name
is
my-machine
computer’s
is
my-machine
client
my-machine
server
mail.yahoo.com

## Slide 6: Reliable Transmission
Higher level of abstraction (transport layer vs. data link layer
client
my-machine
server
mail.yahoo.com
my
computer’s
name
is
my-machine
computer’s my-machine
is
my
name

## Slide 7: Reliable Transmission
Error-correcting codes are not advanced enough to handle the range of bit and burst errors
  Corrupt frames generally must be discarded
  A reliable link-level protocol must recover from discarded frames
Goals for reliable transmission
  Make channel appear reliable
  Maintain packet order (usually)‏
  Impose low overhead / allow full use of link

## Slide 8: Reliable Transmission
Reliability accomplished using acknowledgments and timeouts
  ACK is a small control frame confirming reception of an earlier frame
  Having no ACK, sender retransmits after a timeout
Automatic Repeat reQuest (ARQ) algorithms
  Stop-and-wait
  Concurrent logical channels
  Sliding window
    Go-back-n, or selective repeat
Alternative: forward error correction (FEC)‏

## Slide 9: Automatic Repeat reQuest
Acknowledgement (ACK)‏
  Receiver tells sender when frame received
  Cumulative ACK (used by TCP): have received specified frame and all previous
  Selective ACK (SACK): specifies set of frames received
  Negative ACK (NACK or NAK): receiver refuses to accept frame now, e. g. , when out of buffer space
Timeout: sender decides that frame was lost and tries again
ARQ is also called Positive Acknowledgement with Retransmission (PAR)‏

## Slide 10: Stop-and-Wait
Send a single frame
Wait for ACK or timeout
  If ACK received, continue with next frame
  If timeout occurred, send again (and wait)‏
    Frame lost in transit; or corrupted and discarded
Sender
Receiver
Frame 0
Frame1
ACK0
ACK1

## Slide 11: Design of Stop-and-Wait Protocol

## Slide 12: Acknowledgments and Timeouts

## Slide 13: Stop-and-Wait ARQ
If receiver receives a frame correctly, but sender receives the ACK after timeout …
  Sender resends the frame; how the receiver knows it’s the same frame or the next frame ?
Requires frame identification
  Duplicate frame ?
  Duplicate ACK ?
  1 bit is enough (if physical network maintains order)‏
    sender tracks frame ID to send
    receiver tracks next frame ID expected

## Slide 14: Design of the Stop-and-Wait ARQ Protocol

## Slide 15: Example: Stop-and-Wait ARQ

## Slide 16: Stop-and-Wait ARQ State Diagram
send: 1
expect: 0
send: 0
expect: 0
send: 0
expect: 1
send: 1
expect: 1
receive
frame 0
receive
frame 1
receive
ACK 1
receive
ACK 0
receive frame 0 /
receive ACK 1

## Slide 17: Efficiency of Stop-and-Wait ARQ
Assume that, in a Stop-and-Wait ARQ system, the bandwidth of the line is 1 Mbps, and 1 bit takes 20 ms to make a round trip. What is the bandwidth-delay product? If the system data frames are 1000 bits in length, what is the utilization percentage of the link?
Bandwidth Delay Product
The system can send 20,000 bits during the time it takes for the data to go from the sender to the receiver and then back again.

## Slide 18: Efficiency of Stop-and-Wait ARQ
However, the system sends only 1000 bits. We can say that the link utilization is only 1000/20,000, or 5 percent. Bandwidth Delay Product.
What is the utilization percentage of the link in above example if we have a protocol that can send up to 15 frames before stopping and worrying about the acknowledgments?
The system can send up to 15 frames or 15,000 bits during a round trip. This means the utilization is 15,000/20,000, or 75 percent.

## Slide 19: Stop-and-Wait ARQ
Frames delivered reliably and in order
Is that enough ?
  No, we need performance, too.
Problem: keeping the pipe full … ?
Example
  1.5Mbps link x 45ms RTT = 67.5Kb (~8KB)‏
  1KB frames implies 1KB/45ms= 182 Kbps (1/8th link utilization)‏
  Want the sender to transmit 8 frames before waiting for ACK
  Throughput remains 182 Kbps regardless of the link bandwidth !!

## Slide 20: Concurrent Logical Channels
Multiplex several logical channels over a single p-to-p physical link (include channel ID in header)‏
Use stop-and-wait for each logical channel
Maintain three bits of state for each logical channel:
  Boolean saying whether the channel is currently busy
  Sequence number for frames sent on this channel
  Next sequence number to expect on this channel

## Slide 21: Concurrent Logical Channels
Header for each frame include 3-bit channel number and 1-bit sequence number
  Same number of bits (4) as the sliding window requires to support up to 8 outstanding frames on the link
Characteristics
  Separates reliability from flow control and frame order
  Each channel limited by stop-and-wait bandwidth
  Aggregate bandwidth uses full physical link
  Supports multiple communicating processes
  Can use more than one channel per process
    But no frame ordering between channels

## Slide 22: Approaches for Reliable Transmission …
Stop-and-wait
  Provides reliable, in-order delivery
  Sacrifices performance
Multiple logical channels
  Provides reliable delivery at full link bandwidth
  Sacrifices packet ordering
Sliding window: meets all three goals

## Slide 23: Sliding Window
Allow sender to transmit multiple frames before receiving an ACK, thereby keeping the pipe full
Upper bound on outstanding un-ACKed frames
Also used at the transport layer (by TCP)‏
Sender
Receiver
T
ime
…
…

## Slide 24: Sliding Window Concepts
Consider ordered stream of data
  broken into frames
  stop-and-wait
    window of one frame
    slides along stream over time
Sliding window algorithms generalize this notion
  multiple-frame send window
  multiple-frame receive window
time

## Slide 25: Sliding Window Concepts
Send window
  fixed length, containing numbered frames
  starts at earliest unacknowledged frame
  only frames in window sent over network
  Green: sent and acknowledged
  Red: sent (or can be sent) but not acknowledged
  Blue: available, but not within send window
time

## Slide 26: Sliding Window Concepts
Receive window
  fixed length (unrelated to send window)‏
  starts at earliest unreceived frame
  only frames in window are buffered
  Green: received and delivered
  Red: received and buffered
  Blue: received and discarded
time

## Slide 27: Sliding Window - Sender
Assign sequence number to each frame (SeqNum)‏
Maintain three state variables:
  send window size (SWS)‏
  last acknowledgment received (LAR)‏
  last frame sent (LFS)‏
Maintain invariant: LFS - LAR ≤ SWS
Advance LAR when ACK arrives
Buffer up to SWS frames and associate timeouts
time
14
15
12
13
11
19
20
17
18
16
LAR=13
LFS=18
≤ SWS

## Slide 28: Sliding Window - Receiver
Maintain three state variables
  receive window size (RWS)‏
  largest acceptable frame (LAF)‏
  last frame received (LFR) or next frame expected (NFE)‏
Maintain invariant: LAF – LFR ≤ RWS
Frame SeqNum arrives:
  if LFR ≤ SeqNum ≤ LAF  accept
  if SeqNum ≤ LFR or SeqNum > LAF  discarded
Send cumulative ACKs
time
14
15
12
13
11
19
20
17
18
16
LFR=12
LAF=17
≤ RWS

## Slide 29: Sliding Window Issues
When a timeout occurs, data in transit decreases
  Pipe is no longer full when packet losses occur
  Problem aggravates with delay in packet loss detection
Early detection of packet losses improves performance:
  Negative Acknowledgements (NACKs)‏
  Duplicate Acknowledgements
  Selective Acknowledgements (SACKs)‏
    Adds complexity but helps keeping the pipe full

## Slide 30: Sliding Window Classification
Stop-and-wait: SWS=1, RWS=1
Go-back-N: SWS=N, RWS=1
Selective repeat: SWS=N, RWS=M (usually M = N)‏
selective repeat
go-back-N
stop-and-wait

## Slide 31: Sliding Window: Go-back-N
Go-back-N (SWS=N, RWS=1)‏
Receiver only buffers 1 frame
If frame lost, sender may need to resend N frames
  i. e. , sender goes back N frames
Variations
  How long is the frame timeout?
  Does receiver send NACK for out-of-sequence frame?
Inefficient for a noisy link

## Slide 32: Sliding Window: Go-back-N

## Slide 33: Sliding Window: Go-back-N
Cumulative acknowledgments: Note that although ACK 2 is lost, ACK 3 serves as both ACK 2 and ACK 3

## Slide 34: Sliding Window: Go-back-N
Time Out: Note that before the second timer expires, all outstanding frames have been sent and the timer is stopped.

## Slide 35: Sliding Window: Selective Repeat
Selective repeat (SWS=N, RWS=M)‏
Receiver buffers M frames
If frame lost, sender must resend only
  frames lost within receive window
  frames past end of receive window
Variations
  How long is the frame timeout?
  Use cumulative or per-frame ACK?
  Does protocol adapt timeouts?
  Does protocol adapt SWS and/or RWS?

## Slide 36: Sliding Window: Selective Repeat

## Slide 37: Sliding Window: Selective Repeat
Sender
Receiver

## Slide 38: Sliding Window: Selective Repeat