## Slide 1: CSC- 362 Computer Networks Week-8 Lecture-15-16
                Prepared by:
                Mr. Attique Ur Rehman

## Slide 2: Instructor Contact Details
Name: Mr. Attique Ur Rehman
Course Instructor: CSC362- Computer Networks
Credit Hours: (3+1)=4
Office Location: 2nd Floor Computer Science Faculty Office: 41-C
Email: attique.rehman@lgu.edu.pk
Visiting Hours: Wednesday (11:30 am -1:00 pm)

## Slide 3: Course Material
Reference books
  Many textbooks on Networking may be consulted
Research papers!
RFCs and Internet drafts
  Related to TCP/IP suite and other protocols
Web resources
  Tutorials, white papers, reports, etc.

## Slide 4: Text Book
Computer Networks: A Systems Approach by Larry L. Peterson and Bruce S. Davies.
  Third Edition [2003], Morgan Kaufmann Publishers, San Mateo, California, USA
Computer Networks by Andrew S. Tanenbaum
    Fifth Edition
Data Communication and Computer Networks, by Behrouz A. Forouzan
    5th Edition
Data and Computer Communications by William Stallings
  10th Edition
Computer Networking: A Top-Down Approach Featuring the Internet by James F. Kurose and Keith W. Ross
  6th edition

## Slide 5: The Big Picture
You are here

## Slide 6: What we know …
Elements of networks: nodes and links
Building a packet abstraction on a link
Transmission, and units of communication data
Detecting transmission errors
Simulating an error-free, reliable channel
  Sliding window mechanism
Arbitrating access to a shared medium
Design issues of direct link networks
  Functionality of network adaptors

## Slide 7: What Next …?
LANs do not normally operate in isolation. They are connected to one another or internet
To connect LANs or segments of LANs connecting devices are used.
Connecting devices operates in different layers of internet model.
  This chapter discuss which operates at physical and data link layer

## Slide 8: Connecting Devices
Passive hubs
Repeater/Active hubs
Bridges or two layer switches
Routers or three layer switches
Gateways

## Slide 9: Passive hubs
A passive hub is just a connector
It connects the wires coming from different branches
In star topology Ethernet LAN
  a passive hub is a point where the signal coming from different nodes collide.
The passive hub is a collision point.
Passive hub is a part of transmission media and operate below the physical layer

## Slide 10: Repeater
A repeater is device which operates only in the physical layer
It receives a signal and before, it becomes too weak or corrupted, regenerate the original bit pattern.
The repeater sends the refreshed signal.
A repeater can extend the physical length of a LAN

## Slide 11: Repeater
A repeater connects segments of a LAN.
A repeater forwards every frame – there is no filtering.
A repeater is a regenerator, not an amplifier.

## Slide 12: Function of Repeater

## Slide 13: Active Hubs
An active hub is a multi-port repeater, used in star-wired LANs (Ethernet).
Operate at physical link
Because of the amount of traffic and collisions, hubs can only be used in small network configurations.

## Slide 14: Building Extended LANs
Traditional LAN
  Shared medium (e.g., Ethernet)
  Cheap, easy to administer
  Supports broadcast traffic
Problem
  Scale LAN concept
    Larger geographic area (> O(1 km))
    More hosts (> O(100))
  But retain LAN-like functionality
Solution: bridges

## Slide 15: Bridges
Connect two or more LANs with a bridge
  Operates in both physical and data link layer
    as a physical device, it regenerates the signal it receive.
    as a data link device, it check the MAC address of source and destination contained in the frame.
  Transparently extends a LAN over multiple networks
  Comprises 2 to 4 ports
  accept and forward strategy (in promiscuous mode)
  level 2 connection (does not add packet header)
A
Bridge
B
C
X
Y
Z
Port 1
Port 2

## Slide 16: Switches
Switches like bridges are used to connect the subdivided segments of networks.
It is a Layer 2 devices. Operate at the Data Link Layer (Layer 2) of the OSI Reference Models.
Switches use the best of hubs and bridges while adding more abilities
  Multi-port ability of hub
  Filtering ability of a bridge

## Slide 17: Switches
Switches can perform error checking before forwarding data.
  which are very efficient by not forwarding packets that error-end out or forwarding good packets selectively to correct devices only.
Network Switches and Bridges have many similarities and similar function.
  But Switches are considered as superior devices than bridges.

## Slide 18: Bridges vs. Switches
Packet forwarding
  Bridges are performed using software.
  Switches are performed using hardware/ASICs (Application Specific Integrated Circuits).
Speed
  Switches operate comparatively higher speeds as compared to bridges.
Method of switching
  Bridge is store and forward.
  Switch can be store and forward, cut-through or fragment-free.

## Slide 19: Bridges vs. Switches
Number of Ports
  Switch has more ports than a Bridge.
Operational Mode
  Bridges can operate only in half duplex mode
  Switch can operate both in half duplex or full duplex mode.
  Switches support full-duplex LAN communication.
Collision Domain
  Both Bridge and Switch has one collision domain per port, but switches have one broadcast domain per VLAN.

## Slide 20: Network with Hub-Bridge

## Slide 21: Network with Switch

## Slide 22: Learning Bridges
Trivial algorithm
  Forward all frames on all (other) LAN’s
  Potentially heavy traffic and processing overhead
Optimize by using address information
  “Learn” which hosts live on which LAN
  Maintain forwarding table
  Only forward when necessary (dest. not on same LAN)
  Reduces bridge workload

## Slide 23: Learning Bridges
Learn table entries based on source address
  Timeout entries to allow movement of hosts
Table is an optimization; need not be complete
Always forward broadcast frames
Uses datagram or connectionless forwarding
A
Bridge
B
C
X
Y
Z
Port 1
Port 2
Host Port
A 1
B 1
C 1
X 2
Y 2
Z 2

## Slide 24: A Bridge Connecting two LANs
A bridge does not change the physical (MAC) addresses in a frame.

## Slide 25: A Learning Bridge and Process of Learning

## Slide 26: Learning Bridges
Problem
  Redundancy (desirable to handle failures, but …)
  Makes extended LAN structure cyclic
  Frames may cycle forever (loop problem)
Solution: spanning tree
B3
A
C
E
D
B2
B5
B
B7
K
F
H
B4
J
B1
B6
G
I

## Slide 27: Loop Problem in Learning Bridges
Solution: Spanning Tree

## Slide 28: Spanning Tree
Subset of forwarding possibilities
All LAN’s reachable, but
A cyclic Bridges run a distributed algorithm to calculate the spanning tree
  Select which bridge actively forward
  Developed by Radia Perlman of DEC
  Now IEEE 802.1 specification
  Reconfigurable algorithm

## Slide 29: Spanning Tree Concept
LAN’s and bridges make a bipartite graph
Ports are edges connecting LAN’s to bridges
Spanning tree required
  Connect all LAN’s: all vertices of a graph are covered
  Can leave out bridges: all edges may not be covered

## Slide 30: Spanning Tree Algorithm
Each bridge has a unique, totally-ordered identifier
Select bridge with lowest ID as root bridge
Each bridge determines
  Direction of shortest path to root (preferred port)
  For each connected LAN, is it the designated bridge?
    Select bridge on each LAN closest to root as designated bridge
    Use ID (lowest) to break ties)
  Ports connecting LAN’s to designated bridges called designated ports

## Slide 31: Spanning Tree Algorithm
All designated bridges forward frames
  On all designated ports
  On preferred port (path leading to root)
B3
A
C
E
D
B2
B5
B
B7
K
F
H
B4
J
B1
B6
G
I
B2
LAN
Designated port
Preferred port
Designated bridge

## Slide 32: Example: Prior to Spanning Tree Application
What happens if you have a loop of bridges/switches in your LAN?

## Slide 33: Applying Spanning Tree
Step 1: Select the bridge with smallest ID as root bridge.
Step 2: Mark one port of each bridge (except root bridge) as the root/ proffered port. Root port is the port with least-cost path from the bridge to the root bridge (marked with 1 star).
Step 3: For each LAN, choose a designated bridge. A designated bridge has the least-cost path between the LAN and root bridge (the arrows). Mark the corresponding port that connects the LAN to its designated bridge the designated port (two stars).

## Slide 34: Applying Spanning Tree
Step 4: Mark the root port and designated port as forwarding ports, the others as blocking ports (every port with 1 or 2 stars keep, ports with no stars drop). Note - there is only 1 path between any two bridges.

## Slide 35: Distributed Spanning Tree Algorithm
Bridges exchange configuration messages
  ID for bridge sending the message
  ID for what the sending bridge believes to be root bridge
  Distance (hops) from sending bridge to root bridge
Initially, each bridge believes it is the root
  Sends a configuration message, and checks if any received message is better than the current best message
Each bridge records current best configuration message for each port

## Slide 36: Distributed Spanning Tree Algorithm
Bridges forward configuration messages outward from root bridge i.e., on all designated ports
Bridge assumes it is designated bridge for a LAN until it learns otherwise
B3
A
C
E
D
B2
B5
B
B7
K
F
H
B4
J
B1
B6
G
I

## Slide 37: Algorithm Details
In steady state, only root generates configuration messages periodically
  Timeout restarts algorithm (claiming “I am root …”)
In steady state, only designated bridges forward configuration messages
  Outward from root bridge, to all designated ports
  Until they learn they are not designated bridge
Although algorithm is reconfigurable, it is not possible to forward frames over alternative paths

## Slide 38: Broadcast and Multicast
Forward all broadcast/multicast frames to all preferred and designated ports
  Current practice
  Lets hosts decide whether or not to accept frame
Alternative: extend learning to handle groups
  Learn when no group members downstream
  Group members periodically identify themselves
  Accomplished by having each group member sending a frame to the bridge with group address in source field

## Slide 39: Uses and Limitations of Bridges
Extend LAN concept
Limited scalability
  To O(1,000) hosts
  Not to global networks
Not heterogeneous
  Some use of address, but
  No translation between frame formats

## Slide 40: Limitations of Bridges
Do not scale
  Spanning tree algorithm does not scale
  Broadcast does not scale
Do not accommodate heterogeneity
  Only supports networks with same address formats
Caution: beware of transparency
  Frame drop because of bridge congestion
  Large and variable latency between two hosts
  Frames may reorder in extended LANs

## Slide 41: Routers
A network device that forwards packets form one network to another based on their logical or IP addresses (host-to-host addressing).
Based on routing tables, routers read each incoming packet and decide how to forward it.
Routers work at the network layer (layer 3) of the protocol.
A router normally connects LANs and WANs in internet.

## Slide 42: Routers
Route traffic from one network to other.
It has routing table that is used for making decisions about route.
A routing tables are normally dynamics and updated using routing protocols.
Routers provides additional features like DHCP server, NAT, Static routing,

## Slide 43: Gateway
Device that converts one protocol or format to another
A network gateway converts packets from one protocol to other.
Translate from one protocol to other.
Protocol conversion like VoIP to PSTN or Network Access Control etc.
Does not support dynamic routing

## Slide 44: Gateway
A gateway is normally a computer that operates in all five layers of internet or seven layers of OSI model.
A gateway takes an application message, read it, and interprets it.
It can be used as connecting device between two internetworks that uses different models.
  A network designed to use the OSI model can be connected to another network using the Internet model.
A gateway connecting two systems can
  Take a frame as it arrives from the first system
  Move it up to the OSI application layer
  And remove message

## Slide 45: Implementation and Performance
The cost of processing small packets (parsing headers, deciding output port) dominates other restrictions
  Throughput = packets/sec x bits/packet
Moving data from inputs to outputs in parallel may increase the aggregate throughput
Potential bottlenecks
  I/O bus bandwidth
  Memory bus bandwidth
  Processor computing power