## Slide 1: CSC- 362 Computer Networks Week-9 Lecture:17 & 18
                Prepared by:
                Mr. Attique Ur Rehman

## Slide 2: Packet Switching and Forwarding

## Slide 3: The Big Picture
You are here

## Slide 4
Switching and Forwarding

## Slide 5: Why Switching ?
Motivation:
  Why not just one direct link network?
Basic approach:
  How can we extend the direct link abstraction (provide illusion of one physical network) ?
Challenges:
  What problems must we address ?
Examples:
  Where are these issues addressed in real networks ?
Details of the switch:
  What are the goals in design / how are they addressed ?

## Slide 6: After Switching – Are We Done ?
Heterogeneity
  switching allows multiple physical networks
  but assume one switching strategy
Scale
  direct link networks: O(100) hosts
  packet-switched networks: O(100,000) hosts
  Internet: O(2 year-1974) hosts
Beyond the basics
  quality of service
  congestion and performance analysis
  network trends and their importance

## Slide 7: Connecting Large Networks
Assert: want to use one direct link network
Limitations of directly connected networks:
  Limited Scale - number of hosts that can be attached
    1024 in Ethernet; only 2 in point-to-point link
  Limited geographical area that can be covered
    2500 m in Ethernet; Point-to-point links also limited
Alternative: provide illusion of one physical network
Solution: Indirect connectivity by using switches
  Packet switches in computer networks control frame flow
  Multiple direct link networks, transparent to application

## Slide 8: Packet Switches
A multi-input multi-output device
Local star topology
Performance independent of connectivity
  (e.g. adding new host) if switch is designed with enough aggregate capacity
Maximum degree < physical network limit

## Slide 9: Build Network from Stars
Switches (or stars) to build networks that do not behave like in a star topology

## Slide 10: Forwarding
Packets arrive at one of the several inputs and have to be forwarded / switched to one of the available outputs
  Connectionless and connection-oriented approach to determine the correct output
Which way should it go ?
First challenge: forwarding

## Slide 11: Routing
Forwarding requires information
Second challenge: routing
How to maintain forwarding information ?

## Slide 12: Contention and Congestion
If arrival rate for a certain output is greater than the output capacity, then contention occurs
If arrival rate of packets is too high to cause buffer overflow, then congestion occurs
Who goes first ?
Any one is dropped ?

## Slide 13: Challenges for Packet Switching
Efficient forwarding
  Switch with several output ports
  Decide which output port to use
Routing in dynamic network
  Need information for forwarding
  Construct and maintain the information
Handling contention
  Multiple packets destined for one output port
  Decide which packet goes first
  Decide what to do with others

## Slide 14: Network Layers and Switches
One or more nodes
within the network
User level
OS kernel
host
switch
switch between different physical layers
transport
network
data link
physical
session
presentation
application
network
data link
physical

## Slide 15: Scalable Networks
Switch
  forwards packets from input port to output port
  port selected based on address in packet header
Advantages
  cover large geographic area (tolerate latency)
  support large numbers of hosts (scalable bandwidth)
Input ports
T3
T3
STS-1
T3
T3
STS-1
Switch
Output ports

## Slide 16: Packet Forwarding Analogy
Process of going from one place to another
Focus on decision process at intersections
Path splits, how do you decide which way to go?
How do you navigate at intersections? 3 scenarios:
  from your office to home
  from your home to a new friend’s house (with directions)
  from Airport to the Hotel (without directions)

## Slide 17: Packet Switching / Forwarding
Forwarding: the task of selecting an appropriate output port for a packet
Goals
  Require limited information (both packet and switch)
  Admit efficient implementation
Three approaches
  Datagram or connectionless approach
  Virtual circuit or connection-oriented approach
  Source routing
Important notion: unique global address per host

## Slide 18: Datagram Switching / Forwarding
Every packet contains enough information
  Enables a switch to decide how to forward it
Switch translates global address to output port
  Maintains forwarding/routing table for translations
Each packet forwarded and travels independently
No connection setup phase (connectionless model)
Analogy:
  Postal system: each packet contains complete address for its destination
  Following signs (provided by switches) to reach destination

## Slide 19: Datagram Switching
Managing tables in large, complex networks with dynamically changing topologies is a real challenge for the routing protocol
0
1
3
2
0
1
3
2
0
1
3
2
Switch 3
Host B
Switch 2
Host A
Switch 1
Host C
Host D
Host E
Host F
Host G
Host H
At switch 1:
Dest Port#/Interface
A 2
B 1
C 3
D 0
E 1
… …

## Slide 20: Datagram Switching
What happens if the destination is unknown ?
Network discards packet
  Possibly notifying the sender (“no route to host”)
0
1
3
2
0
1
3
2
0
1
3
2
Switch 3
Host B
Switch 2
Host A
Switch 1
Host C
Host D
Host E
Host F
Host G
Host H
data
B
data
F
data
A
data
C
data
K
E  C
B  A
C  F
D  B
A  K ? ?

## Slide 21: Datagram Model
No round trip time delay waiting for connection setup
  Host can send data anywhere, anytime as soon as it is ready
  Source has no way of knowing if the network is capable of delivering a packet or if the destination host is even up
Packets are treated independently
  Possible to route around link and node failures dynamically
Every packet carry full address of the destination
  Overhead per packet is higher than for the connection-oriented model
  Global address to path translation requires storage
  Might not be possible to deliver packet (dest unknown)

## Slide 22: Virtual Circuit Switching
Explicit connection setup (& tear-down) phase from source to destination: connection-oriented model
  Subsequence packets follow established circuit
Supporting “connections” in network layer may be useful for service notions
Each switch maintains a VC table (connection state) per-link or per-switch
Analogy
  Phone call: each packet follows an established path
  Following a known route to reach the destination

## Slide 23: VC Tables in VC Switching
VC table contains information for each connection
  incoming / outgoing interface (port)
  incoming / outgoing VCI (virtual circuit identifier)
Permanent (PVC) or switched (signaled) virtual circuit (SVC)
Setup message in signaling process (to create VC table) is forwarded like a datagram
Acknowledgment of connection setup to downstream neighbors to complete signaling
  Data transfer phase can start after ACK is received

## Slide 24: Signaling in VC Switching
Setup message is forwarded from Host A to Host B
On connection request, each switch creates an entry in VC table with a VCI for the connection
0
1
3
2
2
1
3
0
0
1
3
2
Switch 3
Host B
Switch 2
Switch 1
Host A
I/F VCI I/F VCI
in in out out
setup
B
setup
B
setup
B
setup
B
2 5 1
I/F VCI I/F VCI
in in out out
2 7 3
I/F VCI I/F VCI
in in out out
3 9 0

## Slide 25: Signaling in VC Switching
Host B accepts connection from Host A, and sends back an ACK
In ACK, everyone communicates its choice of VCI to its upstream neighbor
0
1
3
2
2
1
3
0
0
1
3
2
Switch 3
Host B
Switch 2
Switch 1
Host A
I/F VCI I/F VCI
in in out out
ACK
4
2 5 1
I/F VCI I/F VCI
in in out out
2 7 3
I/F VCI I/F VCI
in in out out
3 9 0
ACK
7
ACK
9
ACK
5
4
7
9

## Slide 26: Data Transfer in VC Switching
Host A knows that everything is in place all the way to Host B
In data packets, each node then puts the VCI of its downstream neighbor
0
1
3
2
2
1
3
0
0
1
3
2
Switch 3
Host B
Switch 2
Switch 1
Host A
I/F VCI I/F VCI
in in out out
data
5
2 5 1 9
I/F VCI I/F VCI
in in out out
2 7 3 4
I/F VCI I/F VCI
in in out out
3 9 0 7
data
9
data
7
data
4

## Slide 27: Virtual Circuit Model
Typically wait full RTT for connection setup before sending first data packet
  Can not avoid failures dynamically; must re-establish connection (old one is torn down to free storage space)
Each data packet contains only a small identifier, making the per-packet header overhead small
  Global address to path information still necessary
Connection setup provides an opportunity to know network conditions and/or reserve resources.
  Avoiding congestion but under-utilizing switch

## Slide 28: Source Routing
All forwarding/topology information required to switch a packet is provided by the source host
Packet header contains sequence of address/ports on path from source to destination
  One direction per switch: port, next switch; (absolute)
  Switches read, use, and then discard directions
Used in some system area networks (SANs)
Directions may be rotated instead of discarding

## Slide 29: Data Transfer in Source Routing
Analogous to following directions
0
1
3
2
2
1
3
0
0
1
3
2
Switch 3
Host B
Switch 2
Switch 1
Host A
data
0
1
3
data
3
0
1
data
1
3
0
data
3
0
1
data
1
0
3
data
2
3
0
1

## Slide 30: Implementation and Performance
Packet arriving at interface 1 has to go on interface 2
Point of contention for packets: I/O and memory bus

## Slide 31: Implementation and Performance
The cost of processing small packets (parsing headers, deciding output port) dominates other restrictions
  Throughput = packets/sec x bits/packet
Moving data from inputs to outputs in parallel may increase the aggregate throughput
Potential bottlenecks
  I/O bus bandwidth
  Memory bus bandwidth
  Processor computing power